| Transmitted by the secretariat | Informal document No. GRRF-69-21 (69th GRRF, 1-4 February 2011 agenda item 2) |
| --- | --- |

Adopted amendments to ECE/TRANS/WP.29/GRRF/2010/29/Rev.1 (Proposal for a new Regulation on Lane Departure Warning System)

I.	Proposal

Paragraph 6.3, should be deleted:

6.3.	Accuracy of the measurements

6.3.1.	Distances shall be measured with an accuracy of +/- 5 cm.

6.3.2.	Speeds shall be measured with an accuracy of +/- 3 km/h.

6.3.3.	Rate of departure accuracy shall be measured with an accuracy of +/- 0.1 m/s.

Paragraph 6.6.1., amend to read:

"6.6.1	Drive the vehicle at a speed of 65 km/h +/- 3 km/h into the centre of the test lane in a smooth manner so that the attitude of the vehicle is stable.

Maintaining the prescribed speed, gently drift the vehicle, either to the left or the right, at a rate of departure of between 0.1 and 0.8 m/s so that the vehicle crosses the lane marking. Repeat the test at a different rate of departure within the range 0.1 and 0.8 m/s."

The road markings of "Japan" are added in Table 1 of Annex3:

Table 1

| PATTERN | COUNTRY | WIDTH |
| --- | --- | --- |
| Left edge lane marking | Centre line | Right edge lane marking |  | Left edge lane marking | Centre line | Right edge lane marking |
|  |  |  |  |  |  |  |  |  |  |  | JAPAN |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  | 10 cm |  |  |  |  | 10 cm |  |  |  | 10 cm |  |  |  |

(*): Excepted certain zones (e.g.: slip road, lane for slow vehicles,…)

The road markings of " Canada " are added in Table 1 of Annex3:

Table 1

| PATTERN | COUNTRY | WIDTH |
| --- | --- | --- |
| Left edge lane marking | Centre line | Right edge lane marking |  | Left edge lane marking | Centre line | Right edge lane marking |
|  | Definition of lane width for the purpose of this Regulation |  |
|  | Traffic Flowing in Opposite Direction |  |
|  | Traffic flowing in same direction |  |
|  | Traffic flowing in opposite directions with lane changing prohibited |  |
|  | Traffic flowing in opposite directions with lane changing allowed only from one lane |  |
|  | Continuity lines in merging and diverging areas |  |
|  | Guiding Lines |  |

# Text boxes

Centrelines yellow, right edge lines white left edge line yellow

3m

6m

Centrelines yellow, right edge lines white left edge line yellow

Centrelines yellow, right edge lines white left edge line yellow

Lane width

Lane width

12m

4m

Centrelines yellow, right edge lines white left edge line yellow

3m

6m

Centrelines white

3m

3m

10 – 15 cm

White Lines

0.5m

0.5m

10-15 cm