|  | United Nations | ST/SG/AC.10/C.3/2012/13 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 3 April 2012 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-first session

Geneva, 25 June – 4 July 2012

Item 2 (f) of the provisional agenda

Explosives and related matters: miscellaneous

Transport of explosives, portable tank instructions

Transmitted by the Australian Explosives Industry Safety Group (AEISG)

Introduction

- The purpose of this proposal is to clarify the portable tank instructions, T1, for explosives of Class 1.

Discussion

- The entries for Explosives, Blasting, Types B and E, UN 0331 and UN 0332 respectively, permit transport in portable tanks, T1.

- The portable tank instructions (refer sections 4.2.5.2.1 and 4.2.5.2.2 of the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, seventeenth revised edition) acknowledge the  inclusion of Class 1 substances.

- However, in 4.2.5.2.6, the tabulated portable tank instructions for T1 – T22 states the following in the header to the table:

“These portable tank instructions apply to liquid and solid substances of Classes 3 to 9. The general provisions of section 4.2.1 and the requirements of section 6.7.2 shall be met.”.

- Substances of Class 1 are not included.

- AEISG sees this as a relatively minor issue but, necessarily, one requiring information to be explicit.

Proposal

- It is proposed to amend the header to the tabulated portable tank instructions for T1 – T22 to read as follows:

“These portable tank instructions apply to liquid and solid substances of Class 1 and Classes 3 to 9. The general provisions of section 6.7.2 shall be met.”.

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).