|  | United Nations | ST/SG/AC.10/C.3/2012/72 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 13 September 2012 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-second session

Geneva, 3 – 11 December 2012
Item 7 of the provisional agenda

New proposals for amendments to the Model Regulations 
on the Transport of Dangerous Goods

Organic peroxides

New formulations to be listed in 2.5.3.2.4 and IBC520

Transmitted by the International Council of Chemical Association (ICCA)

Introduction

1.	Since several new peroxides and formulations have become commercially available, there is a need to update 2.5.3.2.4 and IBC520. A list of new products, proposed classification, the accompanying competent authority approval references and a summary of the supporting test data are given in Annex to this proposal.

Proposals

2.	ICCA proposes to include two amended entries and a correction in 2.5.3.2.4, list of currently assigned organic peroxides, as indicated in 3. Further, ICCA proposes to include two changes in packaging IBC520, as indicated in 4.

3:	Proposed amendments to 2.5.3.2.4 List of currently assigned organic peroxides:

| ORGANIC PEROXIDE | Concentration (%) | Diluent type A (%) | Diluent type B 1) (%) | Inert solid (%) | Water (%) | Packing Method | Control tempe-rature (°C) | Emergency temperature (°C) | Number (Generic entry) | Subsidiary risks and remarks |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Correct: DIBENZOYL PEROXIDE | >51 - 100 |  |  | ≤ 48 |  | OP2 |  |  | 3102 | 3) |
| Into DIBENZOYL PEROXIDE Remark: typing error since 8th revision | >52 - 100 |  |  | ≤ 48 |  | OP2 |  |  | 3102 | 3) |
| Change: DICETYL PEROXYDICARBONATE | ≤ 100 |  |  |  |  | OP7 | +30 | +35 | 3116 |  |
| Into DICETYL PEROXYDICARBONATE | ≤ 100 |  |  |  |  | OP8 | +30 | +35 | 3120 |  |
| tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE | >32-100 |  | ≥ 68 |  |  | OP7 |  |  | 3105 |  |
|  | ≤ 32 |  |  |  |  | OP8 |  |  | 3109 |  |
| Into tert-BUTYL PEROXY-3,5,5-TRIMETHYLHEXANOATE | >37-100 |  | ≥ 63 |  |  | OP7 |  |  | 3105 |  |
|  | ≤ 37 |  |  |  |  | OP8 |  |  | 3109 |  |
| Remark: This change is proposed because in packing instruction IBC520, this product with a concentration of ≤ 37% is already listed as UN 3109 |  |  |  |  |  |  |  |  |  |  |

4.	Proposed amendments to packing instruction IBC520:

| UN No. | Organic peroxide | Type of IBC | Maximum quantity (litres) | Control temperature | Emergency Temperature |
| --- | --- | --- | --- | --- | --- |
| 3119 | ORGANIC PEROXIDE TYPE F, LIQUID, TEMPERATURE CONTROLLED |  |  |  |  |
|  | Add new entry: |  |  |  |  |
|  | 1,1,3,3-Tetramethylbutyl peroxy-2-ethylhexanoate, not more than 67%, in diluent type A | 31HA1 | 1000 | +15 ºC | +20 ºC |
|  | Add to existing entry: |  |  |  |  |
|  | Di-(2-ethylhexyl) peroxydicarbonate, not more than 62%, stable dispersion, in water | 31HA1 | 1000 | -20 ºC | -10 ºC |

Annex: Test results of new organic peroxides and formulations to be added/amended (2.5.3.2.4 or IBC520)

| No | Product | packaging | UN No. | Detonation | P/T / C.1 | Deflagration / C.2 | Koenen/ E.1 | DPVT/ E.2 | (mod) Trauzl F.3 or F.4 | SADT (H.3 or H.4) | Competent Authority approval number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Dicetyl peroxydicarbonate, ≤100% | OP8 | 3120 | Test A.1 No propagation | <2170kPa, No | 0.0 mm/s, No | < 1mm ("O"), No | <1.0 mm (10g), Low | n.a. | H.4 40 °C (400ml) | NL TNO 12EM/562 |
| 2 | Di-(2-ethylhexyl) peroxydicarbonate, not more than 62%, stable dispersion, in water | 31HA1 | 3119 | Test A.1 No propagation | <2170kPa, No | 0.0 mm/s, No | <1.0mm ("O"),No | 1.0 mm (50g), Low | F.4 0.4 ml, Low | H.3 0 °C | NL TNO 08DV3/2133 |
| 3 | 1,1,3,3-Tetramethylbutyl peroxy-2-ethylhexanoate, not more than 67%, in diluent type A | 31HA1 | 3119 | Test A.6 No propagation (90%) | <2170kPa, No (94%) | 0.33 mm/s, No (70%) | <1 mm ("A"), Low (70%) | < 3.5 mm, Low (70%) | F.4 4 ml, Low (70%) | H.3 +30 °C (65%) | NL TNO 11 HPE/612 |

_____________________

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2011-2012 approved by the Committee at its fifth session (refer to ST/SG/AC.10/C.3/76, para. 116 and ST/SG/AC.10/38, para. 16).