UN/SCETDG/41/INF.16

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 16 May 2012 Forty-first session Geneva, 25 June – 4 July 2012 Item 5 (a) of the provisional agenda Miscellaneous proposals of amendments to the Model Regulations on the Transport of Dangerous Goods: packagings

Editorial corrections to paper ST/SG/AC.10/C.3/2012/3 and consequent amendment of Special Provision SP 338

Submitted by the European Cylinder Makers Association (ECMA)

Introduction

- This paper proposes to eliminate two minor editorial errors in working document ST/SG/AC.10/C.3/2012/3 submitted by ECMA. (See Proposal 1)

- SP 338 requires that all UN 3478 articles shall pass the hot water bath test prescribed in Section 6.2.4.1.

- The amendment proposed to Section 6.2.4 contained in ST/SG/AC.10/C.3/2012/3, will, if approved, permit the use of alternative methods of testing UN 3478 articles.

- It is therefore proposed that, following approval of ST/SG/AC.10/C.3/2012/3, and specifically that alternatives to the hot water bath test are permitted in SP 338. (See Proposal 2)

Proposal 1

The following editorial changes shall be made in document ST/SG/AC.10/C.3/2012/3 (changes underlined):

Para 5 of the proposal, 6.2.4.1 – 3rd line shall read: “Each gas cartridge ...... shall be subjected to ......”

6.2.4.1.1.1 – 2nd line – at the end of line, it shall read: “........ (50°C if .........).”

Proposal 2

SP 338 subparagraph (c) shall read (changes underlined):

"(c) Pass the hot water bath test in 6.2.4.1.1 or the alternative set out in 6.2.4.1.2"