UN/SCETDG/42/INF.24

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 20 November 2012 Forty-second session Geneva, 3 – 11 December 2012 Item 2 (c) of the provisional agenda Recommendations made by the Sub-Committee on its thirty-ninth, fortieth and forty-first sessions and pending issues: electric storage systems

Illustration of current practices in the collection of waste lithium batteries

Transmitted by PRBA – The Rechargeable Battery Association and RECHARGE - The International Association for the Promotion and Management of Portable Rechargeable Batteries

Introduction

- PRBA and RECHARGE working paper ST/SG/AC.10/C.3/2012/86 provides for a new Special Provision XXX and Packing Instruction P903a for transporting lithium cells and batteries for disposal or recycling with or without non-lithium cells and batteries.

- ST/SG/AC.10/C.3/2012/86 contains packaging provisions that have been successfully implemented in the United States and in Europe in accordance with ADR where several tenth of thousands of Tonnes per year of batteries have been safely collected and transported for disposal or recycling.

- This INF paper is aimed at supporting ST/SG/AC.10/C.3/2012/86 by providing an illustration of the following elements related to battery collection activities and programs:

The current ratios of lithium batteries placed on the market compared to other battery chemistries in two major EU countries;

Examples of poor packaging practices observed when non-conforming packaging are used; and

Examples of good packaging practices that are used by several National Collection and Recycling Schemes and their logistic partners (collective or private).

- We believe these illustrations will help the Sub-Committee to focus the discussion on practical cases in order to better understand the proposals contained in ST/SG/AC.10/C.3/2012/86.

- This paper has been prepared in cooperation with the following battery collection organizations in Europe and their partners: BEBAT, STIBAT, GRS.

| 1.a. Market date Quantity of Portable Batteries (Primary and Rechargeable) Placed on the Market in Germany and France (2011). The Lithium battery ratio of batteries placed on the market is < 5% for Lithium Metal and 15 % for Lithium-Ion. Figure 1 ( Germany) Figure 2 (France) ___________________________________ Major collection sources for waste Batteries discarded by consumers (Representative of 25’000 Tonnes in 11 EU Member States) >>>> _____________________________________ 2.a. Bad practice Lithium cells not individually protected against short circuits and pack without protection against movement during transport. Figure 1 2.2 E-Bikes Batteries individually protected against short circuits but packed without protection against movement during transport. Figure 2 Disassembled packs represent a major source of hot spots due to short-circuits and residual energy stored in the battery. Figure 3. Other exemples of good practices 3.1 Covering the batteries with vermiculite (filling voids in the container). Figure 1. 3.2 Use of a closed plastic liner and vermiculite to avoid the movement of batteries during transport Figure 2. 3.3 Examples of waste battery individual packaging with a plastic bag Figure 3. Collection tools (EU) 4.1 Between First Collection point and First Consolidation facility (Exempted) The 20 l to 30 l carboard box used in sales points for consumer batteries. Figure 1. The 60 l drum used in schools (e.g.). Figure 2. The 60 l (and others) drum(s) for transport of waste batteries from the first consolidation point to further sorting or processing (PG II Performance Level). Figure 3. | 1.b. Collection data (EU) Quantity of Waste Portable Batteries (Primary and Rechargeable) collected in Germany and France (2011). The Lithium battery content of collected waste batteries is < 1% for Lithium Metal and 2 % for Lithium-Ion. Figure 3 (Germany) Figure 4 (France) Figure 5 2.b. Recommended practice 2.4 When individual cells are not protected, the use of a cushioning material is appropriate. Figure 4. E-Bikes Lithium Batteries individually protected against short circuits and packed against movement during transport by using cushioning material. NB Cushioning material will fill completely the voids in the packaging. Figure 5. Individual protection is required to minimize risks. Figure 6. 3.4 The principle of using cushioning material in a multilayer arrangement. Figure 4. 3.5 Sand is also used as a cushioning material to stabilized the batteries during transport and protect against short circuit Figure 5. 3.6 Keeping Lithium Primary Batteries in a blister is a safe practice Figure 6. 4.2 Between First Collection point and Further treatment facility (sorting of processing) The 60 litres drum for transport of waste batteries from the first consolidation point to further sorting or processing (PG II Performance Level). Figure 4. 4.3 Appropriate Labelling For all shipments, information about the Lithium battery content should be made visible on the packing. Figure 5. |
| --- | --- |