UN/SCETDG/42/INF.70

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 10 December 2012 Forty-second session Geneva, 3 – 11 December 2012

1.5.1.5.1

Note by the secretariat

During the discussion of paragraph 1.5.1.5.1, the representative of IAEA made a remark concerning possible misunderstandings. The secretariat has discussed the issue with the representative of IAEA and proposes the following addition to 1.5.1.5.1 so that the paragraph reads as follows:

1.5.1.5.1	Excepted packages which may contain radioactive material in limited quantities, instruments, manufactured articles and empty packagings as specified in 2.7.2.4.1 shall be subject only to the following provisions of Parts 5 to 7:

(a)	The applicable provisions specified in 5.1.2, 5.1.3.2, 5.1.4, 5.1.5.4, 5.2.1.7 and 7.1.8.5.2;

(b)	The requirements for excepted packages specified in 6.4.4; and

(c)	If the excepted package contains fissile material, one of the fissile exceptions provided by 2.7.2.3.5 shall apply and the requirement of 6.4.7.2 shall be met;

except when the radioactive material possesses other hazardous properties and has to be classified in a class other than Class 7 in accordance with special provision 290 or 369 of Chapter 3.3, where the provisions listed in (a), (b) and (c) above apply only as relevant and in addition to those relating to the main hazard class or division.