|  | United Nations | ECE/TRANS/WP.29/2012/20 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 27 December 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

One-hundred-and-fifty-sixth session

Geneva, 13–16 March 2012

Item 4.10.1 of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by GRSG

Proposal for Supplement 5 to the 02 series of amendments to Regulation No. 34 (Fire risks)

Submitted by the Working Party on General Safety Provisions *

The text reproduced below was adopted by the Working Party on General Safety Provisions (GRSG) at its 101st session. It is based on ECE/TRANS/WP.29/GRSG/2009/21, as amended by the report (ECE/TRANS/WP.29/GRSG/80, para. 12). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.11., amend to read:

"5.11.	The fuel tank ... shall be avoided.

If necessary, measure(s) for charge dissipation shall be provided. However, no charge dissipation system is required for fuel tanks designed for containing a fuel with a flash point of at least 55 °C as referred to in item 5.1. of the communication form in Annex 1, Appendix 2. Determination of the flash point shall be in accordance with ISO 2719:2002.

The manufacturer shall … of these requirements."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.