|  | United Nations | ECE/TRANS/WP.29/2012/29 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 29 December 2011 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

156th session

Geneva, 13-16 March 2012

Item 4.13.1 of the provisional agenda

1958 Agreement – Consideration of draft Corrigenda

to existing Regulations submitted by the secretariat

Proposal for Corrigendum 1 to Revision 6 of Regulation No. 37 (Filament lamps)

Note by the secretariat *

The text reproduced below has been prepared to correct Revision 6 of the Regulation concerning physical errors. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

After paragraph 3.9.5.3.2., add the missing paragraph number 3.10 before "Standard filament lamp", as follows:

"3.9.5.3.2.	Not less than 120 per cent of the minimum limits prescribed for the headlamp type concerned.

3.10.	Standard filament lamps

Additional requirements for standard (étalon) filament lamps are given on the relevant data sheets of Annex 1.

…"

Annex 1,

List of sheets for filament lamps and their sequence in this annex, align to the left, as follows:

"List of sheets for filament lamps and their sequence in this annex:

|  | Sheet number(s) |  |
| --- | --- | --- |
|  | C5W/1 |  |
|  | C21W/1 to 2 |  |
|  | H1/1 to 3 |  |
|  | H3/1 to 4 |  |
|  | H4/1 to 5 |  |
|  | H7/1 to 4 |  |
|  | H8/1 to 4 |  |
|  | H9/1 to 4 |  |
|  | H10/1 to 3 |  |
|  | H11/1 to 4 |  |
|  | H12/1 to 3 |  |
|  | H13/1 to 4 |  |
|  | H14/1 to 4 |  |
|  | H15/1 to 5 |  |
|  | H16/1 to 4 |  |
|  | H6W/1 |  |
|  | H10W/1 to 2 |  |
|  | H21W/1 to 2 |  |
|  | H27W/1 to 3 |  |
|  | HB3/1 to 4 |  |
|  | HB4/1 to 4 |  |
|  | HIR1/1 to 3 |  |
|  | HIR2/1 to 3 |  |
|  | HS1/1 to 5 |  |
|  | HS2/1 to 3 |  |
|  | HS5/1 to 4 |  |
|  | HS5A/1 to 3 |  |
|  | HS6/1 to 4 |  |
|  | P13W/1 to 3 |  |
|  | P19W/1 to 3 |  |
|  | P21W/1 to 2 |  |
|  | P21/4W/1 |  |
|  | P21/5W/1 to 3 |  |
|  | P24W/1 to 3 |  |
|  | P27W/1 to 2 |  |
|  | P27/7W/1 to 3 |  |
|  | PC16W/1 to 3 |  |
|  | PR21W/1 |  |
|  | PR21/4W/1 |  |
|  | PR21/5W/1 |  |
|  | PR27/7W/1 |  |
|  | PSX26W/1 to 3 |  |
|  | PY21W/1 |  |
|  | PY27/7W/1 |  |
|  | R2/1 to 3 |  |
|  | R5W/1 |  |
|  | R10W/1 |  |
|  | S1/S2/1 to 2 |  |
|  | S3/1 |  |
|  | T1.4W/1 |  |
|  | T4W/1 |  |
|  | W2.3W/1 |  |
|  | W3W/1 |  |
|  | W5W/1 |  |
|  | W10W/1 |  |
|  | W15/5W/1 to 3 |  |
|  | W16W/1 |  |
|  | W21W/1 to 2 |  |
|  | W21/5W/1 to 3 |  |
|  | WP21W/1 to 2 |  |
|  | WR21/5W/1 |  |
|  | WY2.3W/1 |  |
|  | WY21W/1 to 2 |  |

"

Sheet H1/1, the drawing, View C, replace the designated angle "€" by "(", as follows:

"

"

Sheet H3/4, the text in the drawing top/left, replace "View A" by "Views A and C" ("and C" was forgotten), to read:

"

"

Sheet H4/1, Figure 1, the drawing, correct the typing mistake of "Axis of bulb".

Sheet H4/2, the table, row "Rated values, Volts", column "Filament lamps of normal production, 24 V", replace "126/" by "246/".

Sheet H4/4, the table, column "Reference*", centre values and replace "IR" and "IC" by "IR" and "IC", as follows:

"

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filaments lamps of normal production | Standard filament lamp |
| 12 V | 24 V | 12 V | 24 V | 12 V | 24 V | 12 V |
| a/26 | 0.8 | (0.35 | (0.20 |
| a/23.5 | 0.8 | (0.60 | (0.20 |
| b1/29.5 | 30.0 | 0 | (0.30 | (0.35 | (0.20 |
| b1/33 | b1/29.5 mv | b1/30.0 mv | (0.30 | (0.35 | (0.15 |
| b2/29.5 | 30.0 | 0 | (0.30 | (0.35 | (0.20 |
| b2/33 | b2/29.5 mv | b2/30.0 mv | (0.30 | (0.35 | (0.15 |
| c/29.5 | 30.0 | 0.6 | 0.75 | (0.35 | (0.20 |
| c/33 | c/29.5 mv | c/30.0 mv | (0.35 | (0.15 |
| d | min. 0.1 | - | - |
| e 13/ | 28.5 | 29.0 | +0.35 -0.25 | (0.35 | +0.20 -0.00 |
| f 11/,12/,13/ | 1.7 | 2.0 | +0.50 -0.30 | (0.40 | +0.30 -0.10 |
| g/26 | 0 | (0.50 | (0.30 |
| g/23.5 | 0 | (0.70 | (0.30 |
| h/29.5 | 30.0 | 0 | (0.50 | (0.30 |
| h/33 | h/29.5 mv | h/30.0 mv | (0.35 | (0.20 |
| IR 11/,14/ | 4.5 | 5.25 | (0.80 | (0.40 |
| IC 11/,14/ | 5.5 | 5.25 | (0.50 | (0.80 | (0.35 |
| p/33 | Depends on the shape of the shield | - | - |
| q/33 | (p+q)/2 | (0.60 | (0.30 |

"

Sheet H4/5, Additional explanations, 1, replace "IR" and "IC" by "IR" and "IC", as follows:

"...

1	For dimensions a, b1, c, d, e, f, IR and IC;

2	For..."

Sheet H8/3, the table, row "Cap:", remove inside borders, to read:

"

| Cap: | H8: PGJ19-1 H8B: PGJY19-1 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| --- | --- | --- |

"

Sheet H9/3, the table, row "Cap:", remove inside borders, to read:

"

| Cap: | H9: PGJ19-5 H9B: PGJY19-5 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| --- | --- | --- |

"

Sheet H11/3, the table, row "Cap:", remove inside borders, to read:

"

| Cap: | H11: PGJ19-2 H11B: PGJY19-2 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| --- | --- | --- |

"

Sheet H13/4, the table, insert inside borders (except for "Cap:" row) and centre 2nd column upper part up to the "Cap:" row), as follows:

"

| Dimensions in mm | Tolerance |
| --- | --- |
|  | Filaments lamps of normal production | Standard filament lamp |
| d1 13/, 17/ | 1.8 max. | - | - |
| d2 13/, 17/ | 1.8 max. | - | - |
| e 16/ | 29.45 | (0.20 | (0.10 |
| f 116/ | 4.6 | (0.50 | (0.25 |
| f 216/ | 4.6 | (0.50 | (0.25 |
| g 8/, 17/ | 0.5 d1 | (0.40 | (0.20 |
| h 8/ | 0 | (0.30 | (0.15 |
| j 10/ | 2.5 | (0.20 | (0.10 |
| k 10/ | 2.0 | (0.20 | (0.10 |
| m 10/ | 0 | (0.20 | (0.13 |
| n 10/ | 0 | (0.20 | (0.13 |
| p 10/ | 0 | (0.08 | (0.08 |
| ( | 42° min. | - | - |
| ( | 52° min. | - | - |
| ( | 43° | +0° / -5° | +0° / -5° |
| ( 9/ | 41° | (4° | (4° |
| Cap: | H13: P26.4t H13A: PJ26.4t | in accordance with IEC Publication 60061 (sheet 7004-128-3) |
| Electrical and photometric characteristics 18/ |
| Rated values | Volts | 12 | 12 |
|  | Watts | 55 | 60 | 55 | 60 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 68 max. | 75 max. | 68 max. | 75 max. |
|  | Luminous flux | 1,100 ( 15% | 1,700 ( 15% |  |
| Reference luminous flux at approximately | 12 V | 800 | 1,200 |
|  | 13.2 V | 1,100 | 1,700 |

"

Sheet H14/3, the table, row "γ3", column "Standard filament lamps", replace "0/5(" by 
"0/-5(" (according to Revision 5, Amendment 2)

"

| Dimensions in mm | Filament lamp of normal production | Standard filament lamps |
| --- | --- | --- |
| e 8/ | 26.15 | 10/ | ±0.1 |
| f1 8/,9/ | 5.3 | 10/ | ±0.1 |
| f2 8/,9/ | 5.0 | 10/ | ±0.1 |
| g | 0.3 min. |  |  |
| h1 | 0 | 10/ | ±0.1 |
| h2 | 0 | 10/ | ±0.15 |
| h3 | 0 | 10/ | ±0.15 |
| h4 | 0 | 10/ | ±0.15 |
| i | 2.7 |  | - |
| j | 2.5 | 10/ | ±0.1 |
| (1 | 55° min. | - | - |
| (2 | 52° min. | - | - |
| (3 | 43° | 0/-5° | 0/-5° |
| Cap P38t in accordance with IEC Publication 60061 (sheet 7004-133-1) |
| Electrical and photometric characteristics |
| Rated values | Volts | 12 | 12 |
|  | Watts | 55 | 60 | 55 | 60 |
| Test voltage | Volts | 13.2 | 13.2 |
| Objective values | Watts | 68 max. | 75 max. | 68 max. | 75 max. |
|  | Luminous flux | 1,150 ± 15% | 1,750 ± 15% |  |  |
| Reference luminous flux at approximately | 12 V | 860 | 1,300 |
|  | 13.2 V | 1,150 | 1,750 |

"

Sheet H15/1, the drawings, Figure 2, move up the parameter "V"; Figure 3, move up the value "4.5"; Figure 4, move up the parameters "γ1" and "γ2"), as follows:

"

"

Sheet H15/4, the table, column "Reference*", centre values and replace "lR" and "lC" by "IR" and "IC", as follows:

"

| Reference* | Dimension** | Tolerance |
| --- | --- | --- |
|  |  | Filament lamps of normal production | Standard filament lamp |
| 12 V | 24 V | 12 V | 24 V | 12 V | 24 V | 12 V | 24 V |
| a/24.0 | a/24.5 | 1.8 | (0.35 | (0.20 |
| a/26.0 | 1.8 | (0.35 | (0.20 |
| b1/31.0 | 0 | (0.30 | (0.15 |
| b1/33.5 | b1/34.0 | b1/31.0 mv | (0.30 | (0.15 |
| b2/31.0 | 0 | (0.30 | (0.15 |
| b2/33.5 | b2/34.0 | b2/31.0 mv | (0.30 | (0.15 |
| c1/31.0 | 0 | (0.30 | (0.50 | (0.15 | (0.25 |
| c1/33.5 | c1/34.0 | c1/31.0 mv | (0.30 | (0.50 | (0.15 | (0.25 |
| c2/33.5 | c2/34.0 | 1.1 | (0.30 | (0.50 | (0.15 | (0.25 |
| d | min. 0.1 | - | - |
| f 8/, 9/, 10/ | 2.7 | (0.30 | (0.40 | +0.20 -0.10 | +0.25 -0.15 |
| g/24.0 | g/24.5 | 0 | (0.50 | (0.70 | (0.25 | (0.35 |
| g/26.0 | 0 | (0.50 | (0.70 | (0.25 | (0.35 |
| h/31.0 | 0 | (0.50 | (0.60 | (0.25 | (0.30 |
| h/33.5 | h/34.0 | h/31.0 mv | (0.30 | (0.40 | (0.15 | (0.20 |
| IR 8/, 11/ | 4.2 | 4.6 | (0.40 | (0.60 | (0.20 | (0.30 |
| IC 8/, 9/ | 4.4 | 5.4 | (0.40 | (0.60 | (0.20 | (0.30 |
| p/33.5 | p/34.0 | Depends on the shape of the shield | - | - |
| q/33.5 | q/34.0 | p/33.5 | p/34.0 | (1.20 | (0.60 |

"

Sheet H15/5, at the end of the last line, delete the quotation mark, to read:

"......

distances of 24.0 mm (24.5 mm for 24 V types) and 26.0 mm.

"

Sheet H16/3, the table, row "Cap:", remove inside borders, to read:

"

| Cap: | H16: PGJ19-3 H16B: PGJY19-3 | in accordance with IEC Publication 60061 (sheet 7004-110-2) in accordance with IEC Publication 60061 (sheet 7004-146-1) |
| --- | --- | --- |

"

Sheet H10W/1, the row "cap", insert IEC sheet numbers according to Revision 5 - Amendment 3 - Corrigendum 1), to read:

"

| Cap: | H10W/1 | BAU9s | in accordance with IEC Publication 60061 (sheet 7004-150A-1) |
| --- | --- | --- | --- |
|  | HY10W | BAUZ9s | in accordance with IEC Publication 60061 (sheet 7004-150B-1) |

"

Sheet H21W/1, the table, the last row, lower the line to reveal the reference luminous flux value for "amber: 300 lm", to read:

"....

| Reference luminous flux at approximately | 12 V | White: 415 lm |
| --- | --- | --- |
|  | 13.2 V | White: 560 lm |
|  | 13.5 V | White: 600 lm Amber: 300 lm |

"

Sheet H21W/2, the drawing, the vertical aligned text, replace "20.2 Reference axis" by "20.0 to Reference plane", as follows:

"

"

Sheet HB3/1, the drawing bottom/left, insert "View A" into the top left of the drawing, to read:

"

"

Sheet HB4/2, the note to γ3, replace the 2nd note 6/ by note 8/, as follows:

"

"

Sheet HS1/4, the table, centre the first column and the last two rows and replace "lR" and "lC" by "IR" and "IC", as follows:

"

| Reference* | Dimensions** | Tolerance |
| --- | --- | --- |
|  |  | Filaments lamps of normal production | Standard filament lamp |
| 6 V | 12 V | 6 V | 12 V | 6 V | 12 V | 12 V |
| a/26 | 0.8 | (0.35 | (0.20 |
| a/25 | 0.8 | (0.55 | (0.20 |
| b1/29.5 | 0 | (0.35 | (0.20 |
| b1/33 | b1/29.5 mv | (0.35 | (0.15 |
| b2/29.5 | 0 | (0.35 | (0.20 |
| b2/33 | b2/29.5 mv | (0.35 | (0.15 |
| c/29.5 | 0.6 | (0.35 | (0.20 |
| c/31 | c/29.5 mv | (0.30 | (0.15 |
| d | min. 0.1 / max. 1.5 | - | - |
| e 13/ | 28.5 | +0.45 / -0.25 | +0.20 / -0.00 |
| f 11/, 12/, 13/ | 1.7 | +0.50 / -0.30 | +0.30 / -0.10 |
| g/26 | 0 | (0.50 | (0.30 |
| g/25 | 0 | (0.70 | (0.30 |
| h/29.5 | 0 | (0.50 | (0.30 |
| h/31 | h/29.5 mv | (0.30 | (0.20 |
| IR 11/, 14/ | 3.5 | 4.0 | (0.80 | (0.40 |
| IC 11/, 12/ | 3.3 | 4.5 | (0.80 | (0.35 |
| p/33 | Depends on the shape of the shield | - | - |
| q/33 | (p+q)/2 | (0.60 | (0.30 |

"

Sheet HS1/5, Additional explanations, 1, replace "IR" and "IC" by "IR" and "IC":

"....

1	For dimensions a, b1, c, d, e, f, IR and IC;

2	For..... "

Sheet P13W/2, the table, fifth row, remove inside borders, as follows:

"....

| P13W Cap PG18.5d-1 PW13W Cap WP3.3x14.5-7 | in accordance with IEC Publication 60061 (sheet 7004-147-1) in accordance with IEC Publication 60061 (sheet 7004-164-1) |
| --- | --- |

...."

Sheet P19W/1, the lower drawing, insert the missing symbol "α", to read:

""

Sheet P21/5W/1, the table, row "x, y", replace the reference to footnote 1 by "1/", as follows:

"...

| x, y | 6, 12 V |  | 1/ |  | 2.8 ( 0.3 |
| --- | --- | --- | --- | --- | --- |

..."

Sheet PR21/5W/1, the dimension in the drawing left top, replace the value "55.0 max." by "45.0 max" (as in Revision 5 of the Regulation), as follows:

"

"

Sheet PSX26W/2, footnotes, lower the footnotes to reveal the notes 4/ and 5/, as follows:

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
| e 5/ | 24.0 4/ | 24.0 (0.25 |
| f 5/ | 4.2 4/ | 4.2 (0.25 |
| (1 6/ | 35.0° min. | 35.0° min. |
| (2 6/ | 58.0° min. | 58.0° min. |
| Cap PG18.5d-3 | in accordance with IEC Publication 60061 (sheet 7004-147-1) |
| Electrical and photometric characteristics |
| Rated values | Voltage | V | 12 | 12 |
|  | Wattage | W | 26 | 26 |
| Test voltage | V | 13.5 | 13.5 |
| Objective values | Wattage | W | 26 max. | 26 max. |
|  | Luminous flux | lm | 500 |  |
|  |  | ( | +10% / –10% |  |
| Reference luminous flux at approximately 12 V | 345 lm |
| Reference luminous flux at approximately 13.2 V | 465 lm |
| Reference luminous flux at approximately 13.5 V | 500 lm |

4/	To be checked by means of a "Box-System"; sheet PSX26W/3.

5/	The ends of the filament are defined as the points where, when the viewing direction is perpendicular to the plane through the filament lead-in wires, the projection of the outside of the end turns crosses the filament axis.

6/	No part of the cap beyond the reference plane shall interfere with angle (2 as shown in Figure 1 on sheet PSX26W/1. The bulb shall be optically distortion free within the angles (1+ (2.
These requirements apply to the whole bulb circumference.

Sheet R5W/1, the table, row Cap, remove inside borders and align "in accordance with..." vertically in the centre, and the sheet numbers in the right cell to the left, as follows:

"....

| Dimensions in mm | Filament lamps of normal production | Standard filament lamp |
| --- | --- | --- |
|  | min. | nom. | max. | 4/ |
| e | 17.5 | 19.0 | 20.5 | 19.0 ( 0.3 |
| Lateral deviation 2/ |  |  | 1.5 | 0.3 max. |
| ( | 60° | 90° | 120° | 90° ( 5° |
| Cap: | R5W: BA15s RR5W: BAW15s | in accordance with IEC Publication 60061 | (sheet 7004-11A-9) 1/ (sheet 7004-11E-1) |
| Electrial and photometric characteristics |
| Rated values | Volts | 65/ | 12 | 24 | 12 |
|  | Watts | 5 | 5 |
| Test voltage | Volts | 6.75 | 13.5 | 28.0 | 13.5 |
| Objective values | Watts | 5.5 max. | 7.7 max. | 5.5 max. |
|  | Luminous flux | R5W | 50 ( 20 % |  |
|  |  | RR5W | 5/ | 12 ( 25 % |  |
| Reference luminous flux at approximately 13.5 V: | White: 50 lm Red: 12 lm |

...."

Sheet R10W/1, the table, row Cap, remove inside borders and align "in accordance with..." vertically in the centre, and the sheet numbers in the right cell to the left, as follows:

"....

| Cap: | R10W: BA15s RY10W: BAU15s RR10W: BAW15s | in accordance with IEC Publication 60061 | (sheet 7004-11A-9) 1/ (sheet 7004-19-2) (sheet 7004-11E-1) |
| --- | --- | --- | --- |

...."

Sheet W21/5W/3, the table, second row, replace the value "905" by "9.5"

"

| Reference | a | h | k |
| --- | --- | --- | --- |
| Dimension | 3.5 | 9.5 | 1.0 |

"

Sheet WR21/5W/1, the drawing, correct to read:

"a = major (high wattage) filament

b = minor (low wattage) filament

"

Sheet WY21W/2, the drawing, bottom line, left, replace the parameter "a" by "b", to read:

Annex 2,

Item 9, correct the font size of the reference to the footnote 2 to read:

"....

Colour of the light emitted: White/selective-yellow/amber/red2.......

..."

Annex 7,

Table 3, insert inside border lines, as follows:

"

| Number of lamps in records | Qualifying limit | Number of lamps in records | Qualifying limit | Number of lamps in records | Qualifying limit |
| --- | --- | --- | --- | --- | --- |
| - 200 201 - 213 214 - 227 228 - 240 241 - 254 255 - 268 269 - 281 282 - 295 296 - 308 309 - 322 323 - 336 337 - 349 350 - 363 364 - 376 377 - 390 391 - 404 405 - 417 418 - 431 432 - 444 445 - 458 459 - 472 473 - 485 486 - 499 500 - 512 513 - 526 527 - 540 | 21 22 23 24 25 26 27 28 29 30 31 32 33 34 35 36 37 38 39 40 41 42 43 44 45 46 | 541 - 553 554 - 567 568 - 580 581 - 594 595 - 608 609 - 621 622 - 635 636 - 648 649 - 662 663 - 676 677 - 689 690 - 703 704 - 716 717 - 730 731 - 744 745 - 757 758 - 771 772 - 784 785 - 798 799 - 812 813 - 825 826 - 839 840 - 852 853 - 866 867 - 880 881 - 893 | 47 48 49 50 51 52 53 54 55 56 57 58 59 60 61 62 63 64 65 66 67 68 69 70 71 72 | 894 - 907 908 - 920 921 - 934 935 - 948 949 - 961 962 - 975 976 - 988 989 - 1,002 1,003 -,1016 1,017 - 1,029 1,030 - 1,043 1,044 - 1,056 1,057 - 1,070 1,071 - 1,084 1,085 - 1,097 1,098 - 1,111 1,112 - 1,124 1,125 - 1,138 1,139 - 1,152 1,153 - 1,165 1,166 - 1,179 1,180 - 1,192 1,193 - 1,206 1,207 - 1,220 1,221 - 1,233 1,234 - 1,249 | 73 74 75 76 77 78 79 80 81 82 83 84 85 86 87 88 89 90 91 92 93 94 95 96 97 98 |

"

Annex 9,

Table 1, insert inside border lines, as follows:

"....

|  | 1 %** | 6.5 %** |
| --- | --- | --- |
|  | Accept | Reject | Accept | Reject |
| First sample size: 125 If the number of non-conforming units is greater than 2 (11) and less than 5 (16) take a second sample size of 125 and assess the 250 | 2 6 | 5 7 | 11 26 | 16 27 |

..."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.