|  | United Nations | ECE/TRANS/WP.29/2012/47 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 12 April 2012 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

157th session

Geneva, 26-29 June 2012

Item 4.9.1 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRRF

Proposal for Supplement 14 to Regulation No. 13-H (Brakes of M1 and N1 vehicles)

Submitted by the Working Party on Brakes and Running Gear *

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-second session clarifying the levels of braking performance that are reasonable in the different positions of the ignition key. It is based on ECE/TRANS/WP.29/GRRF/2011/35/Rev.1 as amended by the report (ECE/TRANS/WP.29/GRRF/72, para. 12 and Annex II). It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee (AC.1) for consideration.

Paragraph 5.2.20.1., amend to read:

"5.2.20.1. 	With the parking brake released, the service braking system shall be able to fulfil the following requirements:

(a)	With the propulsion system on/off control in the ''On'' (''Run'') position, generate a static total braking force at least equivalent to that required by the Type-0 test for service braking performance as prescribed in paragraph 2.1. of Annex 3 to this Regulation,

(b)	During the first 60 seconds after the propulsion system on/off control has been deactivated to the ''Off'' or ''Lock'' position and/or the ignition key has been removed, three brake applications shall generate a static total braking force at least equivalent to that required by the Type-0 test for service braking performance as prescribed in paragraph 2.1. of Annex 3 to this Regulation, and

(c)	After the period mentioned above, or as from the fourth brake application within the 60 second period, whichever occurs first, generate a static total braking force at least equivalent to that required by the Type-0 test for secondary braking performance as prescribed in paragraph 2.2. of Annex 3 to this Regulation.

It should be understood that sufficient energy is available in the energy transmission of the service braking system."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.