|  | United Nations | ST/SG/AC.10/C.3/2013/53 |
| --- | --- | --- |
|  | Secretariat | Distr.: General 3 September 2013 Original: English |

Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-fourth session

Geneva, 25 November – 4 December 2013
Item 2 (b) of the provisional agenda
Listing, classification and packing: 
Classification inconsistencies (application of criteria versus dangerous goods list)

Clarification of the assignment to the entry FORMIC ACID with more than 85% acid by mass (UN 1779)

Transmitted by the International Council of Chemical Associations (ICCA)

Introduction

1.	On the basis of document ST/SG/AC.10/C.3/2004/12, which showed the flashpoint as a function of the concentration, it had been decided to amend the former description of UN 1779 to read as follows:

“FORMIC ACID with more than 85% acid by mass”,
and to add “3” in column (4) of the Dangerous Goods List.

As a consequence a new UN number with the following entries had been added:

|  | (2) | (3) | (4) | (5) |  |
| --- | --- | --- | --- | --- | --- |
| 3412 | FORMIC ACID with not less than 10% but not more than 85% acid by mass | 8 |  | II |  |
| 3412 | FORMIC ACID with not less than 5% but less than 10% acid by mass | 8 |  | III |  |

2.	The decision to take the concentration of 85% as the limit for subsidiary risk 3 for formic acid had been made by the safety experts, since a certain safety margin had been agreed.

| Flashpoint as a function of the concentration |
| --- |
| Concentration % | Flashpoint of formic acid |
| 100 | 48 |
| 95 | 51 |
| 90 | 57 |
| 85 | 65 |
| 80 | 82 |

3.	Within this safety margin, some products with a concentration of slightly more than 85% acid by mass, have a flash point above 60°C.

This fact leads to numerous confusions, because according to the entry UN 1779 subsidiary risk 3 is mandatory and according to the general criteria subsidiary risk 3 does not apply.

This ambiguity and confusion leads very often to call backs and delays during transport.

Proposal

4.	ICCA therefore proposes to add a special provision to the entry for UN 1779 in column (6) to read as follows:

XXX	Subsidiary risk 3 has to be assigned also when the concentration exceeds 85% acid by mass and the flash point is above 60°C.

Justification

5.	The proposed special provision will lead to clarification of the actual regulation. In this way the clearing of transport of Formic acid with concentration > 85% acid by mass and flash point > 60°C would be relieved while at the same time the safety requirements are into account.

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2013-2014 approved by the Committee at its sixth session (refer to ST/SG/AC.10/C.3/84, para. 86 and ST/SG/AC.10/40, para. 14).