UN/SCETDG/43/INF.31

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 14 June 2013 Forty-third session Geneva, 24 – 28 June 2013 Item 2 (a) of the provisional agenda Explosives and related matters: tests and criteria for flash compositions

Editorial corrections to ST/SG/AC.10/C.3/2013/24 - proposed modification of the US Flash Composition Test to measure both detonation and deflagration properties

Transmitted by the expert from the United States of America

The following corrections should be made to the text in ST/SG/AC.10/C.3/2013/24:

1.	On page 2, under the heading “Proposals” paragraph 6, subsection (b), the word “not” in the third line should be stricken so the line should read:  “shall be greater than 15 mm...”

2.	On page 6, under the Heading “Experimental I”, paragraph 2, line two, the number “9” should be replaced by the number “19”.

3.	On page 11, in Table II -12 New Formulations etc., the header in Column 6 should be corrected to read: “Pressure Rise < 6 ms” instead of the present “Pressure Rise > 6 ms.”