UN/SCETDG/43/INF.52

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 26 June 2013 Forty-third session Geneva, 24–28 June 2013 Item 5 (d) of the provisional agenda Transport of gases: miscellaneous

Amendment of P208 for cylinders used to transport adsorbed gases

Transmitted by the Government of the United Kingdom

Introduction

1. 	Following comments from the Sub-Committee of Experts on the proposal set out in informal document INF.6, the United Kingdom would like to put forward a revised text for consideration as an amendment to the Model Regulations.

Proposal

2. 	Amend the recently adopted packing instruction P208 to read:

P208 PACKING INSTRUCTION P208

This instruction applies to Class 2 adsorbed gases.

(1) The following packagings are authorised provided that the general packing requirements of 4.1.6.1. are met: (a) Cylinders constructed as specified in 6.2.2 and in accordance with ISO 11513:2011 or ISO 9809-1:2010; and (b) Cylinders constructed before 1 January 2016 in accordance with 6.2.3 and a specification approved by the competent authorities of the countries of transport and use.