UN/SCETDG/43/INF.59/Rev.1

Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals Sub-Committee of Experts on the Transport of Dangerous Goods 26 June 2013 Forty-third session Geneva, 24 – 28 June 2013 Agenda item 6(h) Miscellaneous proposals for amendments to the Model Regulations on the Transport of Dangerous Goods: portable tanks

Comments on ST/SG/AC.10/C.3/2013/6, alternative proposal

Transmitted by the expert from France and Spain

Proposal

6.7.2.19.8 The internal and external examinations shall ensure that:

(a)	The shell is inspected for pitting, corrosion, or abrasions, dents, distortions, defects in welds or any other conditions, including leakage, that might render the portable tank unsafe for transport. The wall thickness shall be verified by appropriate measurement if this inspection indicates a reduction of wall thickness.

Add the same amendment to 6.7.3.15.8 (a) for tanks

Text in standard EN12972

The underlined text has been adapted to be included in the model rule

5.5 Inspection of the tank exterior

5.5.1 Inspection of the condition of the tank

A complete visual inspection shall be performed to identify any surface defect and indication of a leak such as dampness, softened paint or staining/unusual cleanliness. Any surface defects shall be evaluated by the expert, and if considered necessary paint shall be removed.

The wall thickness shall be verified against that given by the type approval documents by appropriate measurement if the tank shows indication of reduction of wall thickness.

The inspection of the condition of the tank for the initial inspection shall be carried out before the attachment  of any insulation, painting, protective lining or coating. For subsequent inspections sheathing, thermal or other insulation shall be removed only to the extent required to achieve a reliable appraisal of the condition of the tank.