|  | United Nations | ECE/TRANS/WP.29/2013/60 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 11 April 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

160th session

Geneva, 25-28 June 2013

Item 4.9.5. of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by

Proposal for Supplement 1 to the 01 series of amendments to the draft Regulation on Advanced Emergency Braking Systems (AEBS)

Submitted by the Working Party on Brakes and Gear Running*

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-forth session (ECE/TRANS/WP.29/GRRF/74, para. 3). It is based on ECE/TRANS/WP.29/2011/93, as reproduced in Annex II to the report. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Paragraphs 6.4.2.1. and 6.4.2.2., amend to read:

"6.4.2.1.	At least one warning mode shall be provided no later than specified in Table I Column B of Annex 3.

In the case of the vehicles referred to in Table I, row 1 of Annex 3, the warning shall be haptic or acoustic.

In the case of the vehicles referred to in Table I, row 2 of Annex 3, the warning shall be haptic, acoustic or optical

6.4.2.2.		At least two warning modes shall be provided no later than specified in Table I Column C of Annex 3."

Paragraphs 6.5.2.1. and 6.5.2.2., amend to read:

"6.5.2.1.	At least one haptic or acoustic warning mode shall be provided no later than specified in Table I Column E of Annex 3.

6.5.2.2.	At least two warning modes shall be provided no later than specified in Table I Column F of Annex 3."

Annex 3, the table, amend to read:

"

| A | B | C | D | E | F | G | H | Row |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | Stationary target | Moving target |  |
|  | Timing of warning modes | Speed reduction (ref. paragraph 6.4.4.) | Timing of warning modes | Speed reduction (ref. paragraph 6.5.3.) | Target speed (ref. paragraph 6.5.1.) |  |
|  | At least 1 (ref. paragraph 6.4.2.1.) | At least 2 (ref. paragraph 6.4.2.2.) |  | At least 1 (ref. paragraph 6.5.2.1.) | At least 2 (ref. paragraph 6.5.2.2.) |  |  |  |
| M31, N2 > 8 t and N3 | Not later than 1.4 s. before the start of emergency braking phase | Not later than 0.8 s. before the start of emergency braking phase | Not less than 20 km/h | Not later than 1.4 s. before the start of emergency braking phase | Not later than 0.8 s. before the start of emergency braking phase | No impact | 12 ± 2 km/h | 1 |
| N2 ≦ 8 t 2, 4 and M2 2, 4 | Not later than 0.8 s before the start of the emergency braking phase | Before the start of the emergency braking phase 3 | Not less than 10 km/h | Not later than 0.8 s before the start of the emergency braking phase | Before the start of the emergency braking phase 3 | No impact | 67 ± 2 km/h 5 | 2 |

1	Vehicles of category M3 with hydraulic braking system are subject to the requirements of row 2.

2	Vehicles with pneumatic braking systems are subject to the requirements of row 1.

3	Values shall be specified by the vehicle manufacturer at the time of Type Approval (Annex 1, paragraph 15).

4	Manufacturers of vehicles covered by row 2 may elect to gain vehicle Type Approval to the values specified in row 1; in this instance compliance shall be demonstrated with all the values contained in row 1.

5	The values for the target speed in cell H2 shall be reviewed before 1st November 2021."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.