|  | United Nations | ECE/TRANS/WP.29/2013/75/Add.1 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 15 August 2013 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

161st session

Geneva, 12-15 November 2013

Item 4.6.8 of the provisional agenda

1958 Agreement – Consideration of draft amendments 
to existing Regulations submitted by GRE

Proposal for Supplement 6 to the 04 series of amendments to Regulation No. 19 (Front fog lamps)

Submitted by the Working Party on Light and Light-signalling*

Addendum

The text reproduced below was prepared in order to clarify the context of the amendments to Regulation No. 19 introduced by ECE/TRANS/WP.29/2013/75. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration, subject to final review by GRE at its October 2013 session.

Paragraph 6.4.3., amend to read:

"6.4.3.	Photometric requirements

When so adjusted, the front fog lamp shall meet the photometric requirements in the table below (refer also to Annex 4, paragraph 2.2. of this Regulation):

| Designated lines or zones | Vertical position* above h + below h - | Horizontal position* left of v: - right of v: + | Luminous intensity (in cd) | To comply |
| --- | --- | --- | --- | --- |
| Point 1, 2** | +60° | ±45° | 85 max | All points |
| Point 3, 4** | +40° | ±30° |  |  |
| Point 5, 6** | +30° | ±60° |  |  |
| Point 7, 10** | +20° | ±40° |  |  |
| Point 8, 9** | +20° | ±15° |  |  |
| Line 1** | +8° | -26° to +26° | 130 max | All line |
| Line 2** | +4° | -26° to +26° | 150 max | All line |
| Line 3 | +2° | -26° to +26° | 245 max | All line |
| Line 4 | +1° | -26° to +26° | 360 max | All line |
| Line 5 | 0° | -10° to +10° | 485 max | All line |
| Line 6 *** | -2.5° | -10° to +10° | 2700 min | All line |
| Line 7 *** | -6.0° | -10° to +10° | < 50 per cent of max. on line 6 | All line |
| Line 8L and R*** | -1.5° to -3.5° | -22° and +22° | 1,100 min | One or more points |
| Line 9L and R*** | -1.5° to -4.5° | -35° and +35° | 450 min | One or more points |
| Zone D*** | -1.5° to -3.5° | -10° to +10° | 12,000 max | Whole zone |
| * The co-ordinates are specified in degrees for an angular web with a vertical polar axis. ** See paragraph 6.4.3.4. *** See paragraph 6.4.3.2. " |

Insert new a paragraph 6.4.3.2., to read:

"6.4.3.2. 	At the request of the applicant, two front fog lamps constituting a matched pair corresponding to paragraph 4.2.2.5. may be tested separately. In this case the specified requirements for lines 6, 7, 8, 9 and the Zone D in the table in paragraph 6.4.3. apply to half the sum of readings of the right-hand and left-hand side front fog lamp. However each of the two front fog lamps shall meet at least 50 per cent of the minimum value required for line 6. Additionally, each of the two front fog lamps that constitute the matched pair corresponding to paragraph 4.2.2.5. are only required to meet the requirements of line 6 and line 7 from 5° inwards to 10° outwards."

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2010–2014 (ECE/TRANS/208, para. 106 and ECE/TRANS/2010/8, programme activity 02.4), the World Forum will develop, harmonize and update regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.