Proposal for draft 03 series of amendments to Regulation No. 51

(Noise of M and N categories of vehicles)

The purpose of this proposal is to amend classification of vehicle type of the consolidated version of the proposal for draft 03 series of amendments to Regulation No. 51 (Informal document GRB-58-04).

I. Proposal

Paragraph 6.2.2.1., amend to read:

6.2.2.1.

| Veh. Cat. | Vehicles used for the carriage of passengers | Phase 1 | Phase 2 | Phase 3*/ |
| --- | --- | --- | --- | --- |
| M1 | PMR < 120kW/t | 72 | 70 | 68 |
|  | PMR 120kW/t … 160kW/t | 73 | 71 | 69 |
|  | PMR > 160kW/t | 75 | 73 | 71 |
|  | PMR > 200kW/t, no. of seats < 4, R-point height < 450mm | 75 | 74 | 72 |
| M2 | GVW < 2.5 t | 72 | 70 | 69 |
|  | GVW 2.5 t ...3.5 t | 74 | 72 | 71 |
| M2 | GVW > 3.5 t; P < 135 kW | 75 | 73 | 72 |
|  | GVW > 3.5 t; P > 135 kW | 75 | 74 | 72 |
| M3 | P < 150 kW | 76 | 74 | 73 |
|  | P 150 kW … 250 kW | 78 | 77 | 76 |
|  | P > 250 kW | 80 | 78 | 77 |
| Veh. Cat. | Vehicles used for the carriage of goods | Phase 1 | Phase 2 | Phase 3*/ |
| N1 | GVW < 2,5 t | 72 | 71 | 69 |
|  | GVW > 2,5 t | 74 | 73 | 71 |
|  | [Engine Cap. < [ ]cc, PMR(GVW) < 35 kW/t] | [74] | [72] | [70] |
| N2 | P ≤ 135kW | 77 | 75 | 74 |
|  | P > 135 kW | 78 | 76 | 75 |
| N3 | P < 150 kW | 79 | 77 | 76 |
|  | P 150 kW … 250 kW | 81 | 79 | 77 |
|  | P > 250 kW | 82 | 81 | 79 |

Insert new paragraph 6.2.2.2.6.,  to read:

6.2.2.2.6	For vehicle types of category N1 having a maximum authorized mass less than or equal to 2.5t, a PMR (power to mass ratio) of GVM less than or equal to 35kW/t and distance “d” between the front axle and the driver‘s seat R-point is less than 1,100 mm , the limits of vehicles types of category N1 having a maximum authorized mass above 2.5 tons apply.

Paragraph 11.3.1., amend to read:

11.3.1.	As from [6] years after the date of entry into force of the 03 series of amendments for vehicle types other than [N1[[  ]cc, PMR(GVW) < 35 kW/t]) and] N2 as from [8] years after the date of entry into force of the 03 series of amendments for vehicles types of category [N1[[  ]cc, PMR(GVW) < 35 kW/t]) and] N2, Contracting Parties applying this UNECE Regulation shall grant UNECE type-approvals only if the vehicle type to be approved meets the requirements of this UNECE Regulation as amended by the 03 series of amendments.

Paragrph 11.3.3., amend to read:

    - As from [8] years after the date of entry into force of the 03 series of amendments to this Regulation for vehicles other than [N1[[ ]cc, PMR(GVW) < 35 kW/t]) and] N2 and as from [11] years after the date of entry into force of the 03 series of amendments for vehicles types of category [N1[[ ]cc, PMR(GVW) < 35 kW/t]) and] N2, Contracting Parties applying this Regulation may continue granting for national or regional purposes, type approvals and extensions of type approvals to the previous series of amendments to this Regulation.

Paragrph 11.4.2., amend to read:

11.4.2.	As from [10] years after the date of entry into force of the 03 series of amendments for vehicle types other than [N1[[ ]cc, PMR(GVW) < 35 kW/t]),] N2, N3 and M3 and as from [12] years after the date of entry into force of the 03 series of amendments for vehicles types of category [N1[[ ]cc, PMR(GVW) < 35 kW/t]),] N2, N3 and M3, Contracting Parties applying this UNECE Regulation shall grant UNECE typeapprovals only if the vehicle type to be approved meets the requirements of this UNECE Regulation as amended by the 03 series of amendments.

Paragrph 11.4.4., amend to read:

11.4.4. 	As from [12] years after the date of entry into force of the 03 series of amendments to this Regulation for vehicles other than [N1[[ ]cc, PMR(GVW) < 35 kW/t]),] N2, N3 and M3 and as from [15] years after the date of entry into force of the 03 series of amendments for vehicles types of category [N1[[ ]cc, PMR(GVW) < 35 kW/t]),] N2, N3 and M3, Contracting Parties applying this Regulation may continue granting for national or regional purposes, type approvals and extensions of type approvals to the previous series of amendments to this Regulation.]

II. Justification

This proposal intends to consider global vehicle variations. There are two types of N1 having GVM< 2.5t. One is front engine type. The other is flat front vehicle which has the engine under the seat and are typical in Asian countries. The sound limit of the latter type should be considered since sound characteristics of the vehicles are same as that of the N1 having 2.5t<GVM.

The definition of flat front vehicle has been discussed in GRSP for global technical regulation No. 9 concerning pedestrian safety. The definition is the vehicles where the longitudinal distance "d " between the front axle and the driver's seat R-point is less than 1,100 mm according to ECE/TRANS/180/Add.9/Amend.1/Appendix 1.

_______________________________

# Text boxes

d