Committee of Experts on the Transport of Dangerous Goods
and on the Globally Harmonized System of Classification
and Labelling of Chemicals

Sub-Committee of Experts on the Transport of Dangerous Goods

Forty-sixth session

Geneva, 1 – 9 December 2014

Item 7 of the provisional agenda

New proposals for amendments to the Model Regulations on the Transport of Dangerous Goods

N-Aminoethylpiperazine (UN 2815): subsidiary risk 6.1

Transmitted by the expert from the United States of America

Introduction

1.	In the Dangerous Goods list, N-Aminoethylpiperazine is currently listed under entry UN 2815, Class 8, packing group III.

2.	Available data indicates however, that N-Aminoethylpiperazine, currently classified and listed in the Dangerous Goods list as a dermal corrosive, should also be assigned a Division 6.1 subsidiary risk based on dermal toxicity.

3.	Toxicity data supporting this assessment is summarized in the International Uniform Chemical Information Database (IUCLID) compiled by the European Union Registration, Evaluation, Authorisation, and restriction of Chemical substances (EU REACH) consortium. The data sheet for N-Aminoethylpiperazine is contained in the Annex 1 to this document.  The relevant supporting toxicity testing data included in Annex 2 and indicates the dermal toxicity of N-Aminoethylpiperazine is 866 mg/kg.  This toxicity value corresponds to a Dermal Toxic, Packing Group III.

4.	Taking into account the dermal toxicity properties outlined above, and following paragraph 2.0.3 of the Model Regulations (Precedence of hazard characteristics), N-Aminoethylpiperazine would remain to be classified under Class 8, with the addition of subsidiary risk 6.1. It is therefore proposed to make appropriate amendments to the Dangerous Goods List as shown below. A review of the guiding principles has substantiated that no additional amendments other than the addition of the subsidiary risk (i.e. amendments to packing or tank provisions etc.) are necessary.

Proposal

5.	Amend entry 2815 in the Dangerous Goods List to read as follows:

| UN No. | Name and description | Class or division | Subsidiary risk | UN packing group | Special provisions | Limited and excepted quantities | Packagings and IBCs | Portable tanks and bulk containers |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  | Packing instruction | Special provisions | Instruction | Special provisions |
| (1) | (2) | (3) | (4) | (5) | (6) | (7a) | (7b) | (8) | (9) | (10) | (11) |
| 2815 | N-Aminoethylpiperazine | 8 | 6.1 | III |  | 5 L | E1 | P001 IBC03 LP01 |  | T4 | TP1 |

Annex 	1			[English only]

DATA SHEET TO BE SUBMITTED TO THE UNITED NATIONS

FOR NEW OR AMENDED CLASSIFICATION OF SUBSTANCES

Submitted by……..United States	Date….4 September 2014

Supply all relevant information including sources of basic classification data. Data should relate to the product in the form to be transported. State test methods. Answer all questions - if necessary state "not known" or "not applicable" - If data is not available in the form requested, provide what is available with details. Delete inappropriate words.

Section 1. SUBSTANCE IDENTITY

1.1	Chemical name	N-Aminoethylpiperazine

1.2	Chemical formula 	C6H15N3

1.3	Other names/synonyms	2-piperazin-1-ylethanamine

1.4.1	UN number 	2815	1.4.2		CAS number 	140-31-8

1.5	Proposed classification for the Recommendations

1.5.1	Proper shipping name (3.1.2) N-Aminoethylpiperazine

1.5.2	Class/division   8	…. subsidiary risk(s)   6.1

packing group   III

1.5.3	Proposed special provisions, if any  Not Applicable

1.5.4	Proposed packing instruction(s)  Not Applicable ………………….

Section 2. PHYSICAL PROPERTIES

2.1	Melting point or range ………..-19 °C

2.2	Boiling point or range ………...220.4 °C

2.3	Relative density at:

2.3.1……15 °C

2.3.2……20 °C	0.98 g/cm3

2.3.3……50 °C

2.4	Vapour pressure at:

2.4.1……50 °C		5.15 Pa @ 20 °C

2.4.2……65 °C

2.5	Viscosity at 20 °C ……………….14.1 mPa – sec @ 20 °C

2.6	Solubility in water at 20 °C ……..g/100ml  > 100 g/l

2.7	Physical state at 20°C (2.2.1.1)	liquid

2.8	Appearance at normal transport temperatures, including colour and odour
Clear liquid; Amine odor

2.9	Other relevant physical properties

Section 3. FLAMMABILITY

3.1	Flammable vapour

3.1.1	Flash point (2.3.3) 99 °C cc

3.1.2	Is combustion sustained? (2.3.1.3)	no

3.2	Autoignition temperature 	>300 °C

3.3	Flammability range (LEL/UEL) 1.1 – 9.4 %

3.4	Is the substance a flammable solid? (2.4.21)	no

3.4.1 If yes, give details

Section 4. CHEMICAL PROPERTIES

4.1	Does the substance require inhibition/stabilization or other treatment such as nitrogen blanket to prevent hazardous reactivity ?		no

If yes, state:

4.1.1	Inhibitor/stabilizer used

4.1.2	Alternative method

4.1.3	Time effective at 55 °C

4.1.4	Conditions rendering it ineffective

4.2	Is the substance an explosive according to paragraph 2.1.1.1? (2.11) no

4.2.1	If yes, give details

4.3	Is the substance a desensitized explosive? (2.4.2.41) no

4.3.1	If yes, give details

4.4	Is the substance a self-reactive substance? (2.4.11) no

If yes, state:

4.4.1	Exit box of flow chart

What is the self-accelerating decomposition temperature (SADT) for a 50 kg package? ..................°C

Is the temperature control required? (2.4.2.3.41) 	yes/no

4.4.2	Proposed control temperature for a 50 kg package		°C

4.4.3	Proposed emergency temperature for a 50 kg package		°C

4.5	Is the substance pyrophoric? (2.4.31) 	no

4.5.1 	If yes, give details

4.6	Is the substance liable to self-heating? (2.4.31) 		no

4.6.1	If yes, give details

4.7	Is the substance an organic peroxide (2.5.1) 		no

If yes state:

4.7.1	Exit box of flow chart

What is the self accelerating decomposition temperature (SADT) for a 50 kg package? ……………°C

Is temperature control required? (2.5.3.4.11) 	yes/no

4.7.2	Proposed control temperature for a 50 kg package		°C

4.7.3	Proposed emergency temperature for a 50 kg package		°C

4.8	Does the substance in contact with water emit flammable gases? (2.4.41) 	no

4.8.1	If yes, give details

4.9	Does the substance have oxidizing properties (2.5.11)	no

4.9.1	If yes, give details	.

4.10	Corrosivity (2.81) to:

4.10.1 ……mild steel 	0.005 mm/year 	at 25 °C

4.10.2 ……aluminium	mm/year  	at	°C

4.10.3 ……other packaging materials (specify)

mm/year	at	°C

mm/year	at	°C

4.11	Other relevant chemical properties  None

Section 5. HARMFUL BIOLOGICAL EFFECTS

5.1	LD50, oral (2.6.2.1.11)    2140 mg/kg  Rat

5.2	LD50, dermal (2.6.2.1.21)   866 mg/kg  Rabbit

5.3	LC50, inhalation (2.6.2.1.31)	mg/l	Exposure time	hours

or	 6 ml/m3	Animal species

5.4	Saturated vapour concentration at 20 °C (2.6.2.2.4.31)   50 - 75 ppm

5.5	Skin exposure (2.81) results   30 - 60 minutes  Rabbit

5.6	Other data     PG III

5.7	Human experience

Section 6. SUPPLEMENTARY INFORMATION

6.1	Recommended emergency action

6.1.1	Fire (include suitable and unsuitable extinguishing agents)

6.1.2	Spillage

6.2	Is it proposed to transport the substance in:

6.2.1	Bulk Containers (6.81)	yes

6.2.2	Intermediate Bulk Containers (6.51)?  yes

6.2.3	Portable tanks (6.71)?	yes

If yes, give details in Sections 7, 8 and/or 9.

Section 7. BULK CONTAINERS (only complete if yes in 6.2.1)

7.1	Proposed type(s)  Currently Authorized Containers

Section 8. INTERMEDIATE BULK CONTAINERS (IBCs) (only complete if yes in 6.2.2)

8.1	Proposed type(s)  Currently Authorized IBCs

Section 9. MULTIMODAL TANK TRANSPORT (only complete if yes in 6.2.3)

9.1	Description of proposed tank (including IMO tank type if known)   Currently Authorized Tanks

9.2	Minimum test pressure

9.3	Minimum shell thickness

9.4	Details of bottom openings, if any

9.5	Pressure relief arrangements

9.6	Degree of filling

  - Unsuitable construction materials ………………………………………………………………………………

Annex 2											[English only]

# Footnotes

In accordance with the programme of work of the Sub-Committee for 2013-2014 approved by the Committee at its sixth session (refer to ST/SG/AC.10/C.3/84, para. 86 and ST/SG/AC.10/40, para. 14).

2 	See definition of "liquid" in 1.2.1 of the Model Regulations on the Transport of Dangerous Goods.

1 		This and similar references are to chapters and paragraphs in the Model Regulations on the Transport of Dangerous Goods.

1		This and similar references are to chapters and paragraphs in the Model Regulations on the transport of Dangerous Goods.

# Text boxes

__________________