| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals 17 April 2014 |
| --- |
| Sub-Committee of Experts on the Transport of Dangerous Goods | Sub-Committee of Experts on the Globally Harmonized System of Classification and Labelling of Chemicals |
| Forty-fifth session | Twenty–seventh session |
| Geneva, 23 June – 2 July 2014 Item 10 (c) of the provisional agenda Issues relating to the Globally Harmonized System of Classification and Labelling of Chemicals: pyrophoric gases | Geneva, 2 – 4 July 2014 Item 3 (g) of the provisional agenda Classification criteria and related hazard communication: miscellaneous |

UN/SCETDG/45/INF.7 UN/SCEGHS/27/INF.4

Proposal to include pyrophoric gas as a hazard category in the flammable gases hazard class of the GHS (track-changes)

Transmitted by the expert from the United States of America

1.	This document contains the text of GHS Chapter 2.2, Annex 1 and Annex 3, as amended in accordance with the proposed list of amendments in document ST/SG/AC.10/C.3/2014/54–ST/SG/AC.10/C.4/2014/5.  Amendments are shown in visible mode (“track-changes”).

2.	Where no change is proposed for certain hazard or precautionary statements assigned to flammable gases in Annex 3, Sections 1 and 2, the text is highlighted for the convenience of the Sub-committee of Experts on the GHS.  Experts are invited to consider whether the full title of the hazard chapter should be included in the assignment.

Annex

Amendments to Chapter 2.2

“CHAPTER 2.2

FLAMMABLE GASES

2.2.1	Definitions

2.2.1.1	A flammable gas is a gas having a flammable range with air at 20 °C and a standard pressure of 101.3 kPa.

2.2.1.2	A pyrophoric gas is a flammable gas that is liable to ignite spontaneously in air at a temperature of 54 ºC or below.

2.2.1.3	A chemically unstable gas is a flammable gas that is able to react explosively even in the absence of air or oxygen.

2.2.2	Classification criteria

2.2.2.1	A flammable gas is classified in one of the two categories for this class according to the following table:

Table 2.2.1:  Criteria for flammable gases

| Category | Criteria |
| --- | --- |
| 1 | Gases, which at 20 °C and a standard pressure of 101.3 kPa: (a) are ignitable when in a mixture of 13% or less by volume in air; or (b) have a flammable range with air of at least 12 percentage points regardless of the lower flammable limit. |
| 2 | Gases, other than those of Category 1, which, at 20 °C and a standard pressure of 101.3 kPa, have a flammable range while mixed in air. |

NOTE 1: 	Ammonia and methyl bromide may be regarded as special cases for some regulatory purposes.

NOTE 2: 	Aerosols should not be classified as flammable gases. See Chapter 2.3.

2.2.2.2	A flammable gas is additionally classified as pyrophoric if it meets the criteria in the following table:

Table 2.2.2:  Criteria for pyrophoric gases

| Category | Criteria |
| --- | --- |
| Pyrophoric gas | Flammable gases that ignite spontaneously in air at a temperature of 54 ºC or below. |

NOTE 1: 	Spontaneous ignition for pyrophoric gases is not always immediate, and there may be a delay.

NOTE 2:		In the absence of data on its auto-ignition temperature, a flammable gas mixture is classified as a pyrophoric gas if it contains more than 1% (by volume) of pyrophoric component(s).

2.2.2.3	A flammable gas that is also chemically unstable is additionally classified in one of the two categories for chemically unstable gases using the methods described in Part III of the UN Manual of Tests and Criteria according to the following table:

Table 2.2.3: Criteria for chemically unstable gases

| Category | Criteria |
| --- | --- |
| A | Flammable gases which are chemically unstable at 20°C and a standard pressure of 101.3 kPa |
| B | Flammable gases which are chemically unstable at a temperature greater than 20°C and/or a pressure greater than 101.3 kPa |

2.2.3	Hazard communication

2.2.3.1	General and specific considerations concerning labelling requirements are provided in Hazard communication: Labelling (Chapter 1.4). Annex 1 contains summary tables about classification and labelling. Annex 3 contains examples of precautionary statements and pictograms which can be used where allowed by the competent authority.

## Table 2.2.4:  Label elements for flammable gases

|  |  | Additional sub-categories |
| --- | --- | --- |
|  | Flammable gas | Pyrophoric gas | Chemically unstable gas |
|  | Category 1 | Category 2 | Pyrophoric gas | Category A | Category B |
| Symbol | Flame | No symbol | Flame | No additional symbol | No additional symbol |
| Signal word | Danger | Warning | Danger | No additional signal word | No additional signal word |
| Hazard statement | Extremely flammable gas | Flammable gas | May ignite spontaneously if exposed to air | May react explosively even in the absence of air | May react explosively even in the absence of air at elevated pressure and/or temperature |

2.2.3.2	If a flammable gas or gas mixture is additionally classified in one or more sub-categories, then all relevant classification(s) should be communicated on the safety data sheet as specified in Annex 4, and the relevant hazard communication elements included on the label.

2.2.4	Decision logic and guidance

The decision logic and guidance, which follow, are not part of the harmonized classification system, but have been provided here as additional guidance. It is strongly recommended that the person responsible for classification studies the criteria before and during use of the decision logic.

2.2.4.1	Decision logic for flammable gases

To classify a flammable gas, data on its flammability are required. The classification is according to decision logic 2.2 (a).

Decision logic 2.2 (a)

2.2.4.2	Decision logic for pyrophoric gases

To classify a flammable gas as a pyrophoric gas, data on its ability to ignite in air are required. The classification is according to decision logic 2.2 (b).

Decision logic 2.2 (b)

2.2.4.3	Decision logic for chemically unstable gases

To classify a flammable gas as chemically unstable, data on its chemical instability are required. The classification is according to decision logic 2.2 (c).

#### Decision logic 2.2 (c)

2.2.4.4	Guidance

2.2.4.4.1	Flammability should be determined by tests or by calculation in accordance with methods adopted by ISO (see ISO 10156:2010 “Gases and gas mixtures – Determination of fire potential and oxidizing ability for the selection of cylinder valve outlets”). Where insufficient data are available to use these methods, tests by a comparable method recognized by the competent authority may be used.

2.2.4.4.2	Pyrophoricity should be determined in accordance with either IEC 60079-20-1 ed1.0 (2010-01) “Explosive atmospheres - Part 20-1: Material characteristics for gas and vapour classification - Test methods and data” or DIN 51794 “Determining the ignition temperature of petroleum products”.

2.2.4.4.3	The classification procedure for pyrophoric gases need not be applied when experience in production or handling shows that the substance or mixture does not ignite spontaneously on coming into contact with air at a temperature of 54 ºC or below.

2.2.4.4.4	Chemical instability should be determined in accordance with the method described in Part III of the Manual of Tests and Criteria. If the calculations in accordance with ISO 10156:2010 show that a gas mixture is not flammable it is not necessary to carry out the tests for determining chemical instability for classification purposes.

2.2.5	[The example in 2.2.5 remains unchanged]”

Amendments to Annex 1, Table A1.2

A1.2		Flammable gases (see Chapter 2.2 for classification criteria)

| Classification | Labelling | Hazard statement codes |
| --- | --- | --- |
| Hazard class | Hazard category | Pictogram | Signal word | Hazard statement |  |
|  |  | GHS | UN Model Regulationsa |  |  |  |
| Flammable gases | 1 |  |  | Danger | Extremely flammable gas | H220 |
|  | 2 | No pictogram | Not required | Warning | Flammable gas | H221 |
|  | Pyrophoric gas |  |  | Danger | May ignite spontaneously if exposed to air | H232 |
|  | A (chemically unstable gases) | No additional pictogram | Not required | No additional signal word | Additional hazard statement: May react explosively even in the absence of air | H230 |
|  | B (chemically unstable gases) | No additional pictogram | Not required | No additional signal word | Additional hazard statement: May react explosively even in the absence of air at elevated pressure and/or temperature | H231 |

a	Under the UN Recommendations on the Transport of Dangerous Goods, Model Regulations, the symbol, number and border line may be shown in black instead of white. The background colour stays red in both cases.”

Amendments to Annex 3, Table A3.1.1

| Code | Physical hazard statements | Hazard class (GHS chapter) | Hazard category |
| --- | --- | --- | --- |
| (1) | (2) | (3) | (4) |
| H230 | May react explosively even in the absence of air | Flammable gases (chapter 2.2) | A (Chemically unstable gases) |
| H231 | May react explosively even in the absence of air at elevated pressure and/or temperature | Flammable gases (chapter 2.2) | B (Chemically unstable gases) |
| H232 | May ignite spontaneously if exposed to air | Flammable gases (chapter 2.2) | Pyrophoric gas |

(The remainder of the table remains unchanged)

Amendments to Annex 3, Section 2, Table A3.2.2

(Only the rows containing amendments are reproduced here. The remainder of the tables remain unchanged)

Table A3.2.2:  Codification of prevention precautionary statements

|  | Prevention precautionary statements | Hazard class | Hazard category | Conditions for use |
| --- | --- | --- | --- | --- |
| (1) | (2) | (3) | (4) | (5) |
| P202 | Do not handle until all safety precautions have been read and understood. | Flammable gases (chapter 2.2) | A, B (chemically unstable gases) |  |
|  |  | Germ cell mutagenicity (chapter 3.5) | 1A, 1B, 2 |  |
|  |  | Carcinogenicity (chapter 3.6) | 1A, 1B, 2 |  |
|  |  | Reproductive toxicity (chapter 3.7) | 1A, 1B, 2 |  |
| P222 | Do not allow contact with air. | Flammable gases (chapter 2.2) | Pyrophoric gas | – if emphasis of the hazard statement is deemed necessary |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 | – if emphasis of the hazard statement is deemed necessary. |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
| P233 | Keep container tightly closed. | Flammable gases (chapter 2.2) | Pyrophoric gas |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3 | – if the liquid is volatile and may generate an explosive atmosphere. |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Acute toxicity, inhalation (chapter 3.1) | 1, 2, 3 | – if the chemical is volatile and may generate a hazardous atmosphere. |
|  |  | Specific target organ toxicity, single exposure; respiratory tract irritation (chapter 3.8) | 3 |  |
| P280 | Wear protective gloves/protective clothing/eye protection/face protection. | Explosives (chapter 2.1) | Unstable explosives and divisions 1.1, 1.2, 1.3, 1.4, 1.5 | Manufacturer/supplier or the competent authority to specify the appropriate type of equipment. |
|  |  | Flammable gases (chapter 2.2) | Pyrophoric gas |  |
|  |  | Flammable liquids (chapter 2.6) | 1, 2, 3, 4 |  |
|  |  | Flammable solids (chapter 2.7) | 1, 2 |  |
|  |  | Self-reactive substances and mixtures (chapter 2.8) | Types A, B, C, D, E, F |  |
|  |  | Pyrophoric liquids (chapter 2.9) | 1 |  |
|  |  | Pyrophoric solids (chapter 2.10) | 1 |  |
|  |  | Self-heating substances and mixtures (chapter 2.11) | 1, 2 |  |
|  |  | Substances and mixtures which, in contact with water, emit flammable gases (chapter 2.12) | 1, 2, 3 |  |
|  | Remainder of P280: unchanged |  |  |  |

Amendments to Annex 3, Section 3, matrix for flammable gases in A3.3.5

| FLAMMABLE GASES (Chapter 2.2) (Flammable gases) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| 1 | Danger | H220 | Extremely flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. No smoking. | P377 Leaking gas fire: Do not extinguish, unless leak can be stopped safely. P381 In case of leakage, eliminate all ignition sources. | P403 Store in a well-ventilated place. |  |

| FLAMMABLE GASES (Chapter 2.2) (Flammable gases) |
| --- |
|  |  |  | Symbol No symbol |
| Hazard category | Signal word | Hazard statement |  |
| 2 | Warning | H221 | Flammable gas |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P210 Keep away from heat, hot surfaces, sparks, open flames and other ignition sources. No smoking. | P377 Leaking gas fire: Do not extinguish, unless leak can be stopped safely. P381 In case of leakage, eliminate all ignition sources. | P403 Store in a well-ventilated place. |  |

| FLAMMABLE GASES (Chapter 2.2) (Pyrophoric gases) |
| --- |
|  |  |  | Symbol Flame |
| Hazard category | Signal word | Hazard statement |  |
| Pyrophoric gas | Danger | H232 | May ignite spontaneously if exposed to air |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P222 Do not allow contact with air. – if emphasis of the hazard statement is deemed necessary. P233 Keep container tightly closed. P280 Wear protective gloves/protective clothing/eye protection/face protection. Manufacturer/supplier or the competent authority to specify the appropriate type of equipment. |  |  |  |

Note: This table lists only the precautionary statement that is assigned due to the pyrophoricity of the gas. For the other precautionary statements that are assigned based on the flammability, see the respective tables for flammable gases.

| FLAMMABLE GASES (Chapter 2.2) (Chemically unstable gases) |
| --- |
|  |  |  | Symbol No additional symbol |
| Hazard category | Signal word | Hazard statement |  |
| A | No additional signal word | H230 | May react explosively even in the absence of air |  |
| B | No additional signal word | H231 | May react explosively even in the absence of air at elevated pressure and/or temperature |  |
| Precautionary statements |
| Prevention | Response | Storage | Disposal |
| P202 Do not handle until all safety precautions have been read and understood. |  |  |  |

Note: This table lists only the precautionary statement that is assigned due to the chemical instability of the gas. For the other precautionary statements that are assigned based on the flammability see the respective tables for flammable gases.

# Footnotes

In the absence of data on its auto-ignition temperature, a flammable gas mixture is classified as a pyrophoric gas if it contains more than 1% (by volume) of pyrophoric component(s).

# Text boxes

At 20 °C and a standard pressure of 101.3 kPa, does it:

(a)	ignite when in a mixture of 13% or less by volume in air?; or

(b)	have a flammable range with air of at least 12 percentage points regardless of the lower flammable limit?

Category 1

Danger

# Yes

Does it have a flammable range with air at 20 °C and a standard pressure of 101.3 kPa?

Category 2

No symbol

Warning

Not classified

Yes

No

No

Gaseous substance or mixture of gases

Go to decision logics 2.2 (b) and 2.2 (c)

Go to decision logics 2.2 (b) and 2.2 (c)

Does the flammable gas or gas mixture ignite spontaneously in air at a temperature of 54 ºC or below1?

Flammable gas or gas mixture

Pyrophoric gas

Danger

Yes

Flammable gas or gas mixture

Category A 
(chemically unstable gas)

No additional symbol

No additional signal word

Yes

Is it chemically unstable at 20 °C temperature and a standard pressure of 101.3 kPa?

No

Category B 
(chemically unstable gas)

No additional symbol

No additional signal word

Yes

Is it chemically unstable at a temperature greater than 20 °C and/or a pressure greater than 101.3 kPa?

No

Not classified as 
chemically unstable