|  | United Nations | ECE/TRANS/WP.29/2014/47 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 March 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

163rd session

Geneva, 24-27 June 2014

Item 4.9.3 of the provisional agenda

1958 Agreement – Consideration of draft amendments
to existing Regulations submitted by GRRF

Proposal for Supplement 19 to Regulation No. 54 (Tyres for commercial vehicles and their trailers)

Submitted by the Working Party on Brakes and Running Gear *

The text reproduced below was adopted by the Working Party on Brakes and Running Gear (GRRF) at its seventy-fifth session (ECE/TRANS/WP.29/GRRF/75, para. 30). It is based on ECE/TRANS/WP.29/GRRF/2013/19, not amended. It is submitted to the World Forum for Harmonization of Vehicle Regulations (WP.29) and to the Administrative Committee AC.1 for consideration.

Annex 5, part I, table A, add the following entries:

"

| Tyre-size designation (+) | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
|  |  |  | Radial | Diagonal | Radial | Diagonal |
| … 4.10/3.50-6 3.50-8 4.40-10 | 2.5 2.5 3.5 | 152 203 254 | - - - | 320 394 480 | - - - | 95 103 124 |

"

Annex 5, part I, table D, add the following entry:

"

| Tyre-size designation (+) | Measuring rim width code | Nominal rim diameter d (mm) | Outer diameter D (mm) | Section width S (mm) |
| --- | --- | --- | --- | --- |
| Code Designated… |
| … 16.5x6.5-8 | 5.375 | 203 | 411 | 165 |

"

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.