|  | United Nations | ECE/TRANS/WP.29/AC.3/39 |
| --- | --- | --- |
|  | Economic and Social Council | Distr.: General 28 March 2014 Original: English |

Economic Commission for Europe

Inland Transport Committee

World Forum for Harmonization of Vehicle Regulations

163rd session

Geneva, 24-27 June 2014

Item 17.8 of the provisional agenda

Progress on the development of new UN Global Technical Regulations (UN GTRs)
and of amendments to established UN Global Technical Regulations (UN GTRs)

Gtr No. 15 (Worldwide harmonized Light vehicles Test Procedures – Phase 1(b))

Authorization to develop amendments to gtr No. 15 on the Worldwide harmonized Light vehicles Test Procedures (WLTP)

Submitted by the representative of the European Union*

The text reproduced below to amend gtr No. 15 and to prolong the mandate of the WLTP informal working group was adopted by the Administrative Committee of the 1998 Agreement at its March 2014 session (ECE/TRANS/WP.29/1108, para. 100). It is based on ECE/TRANS/WP.29/2014/30, not amended. This authorization is transmitted to the Working Party on Pollution and Energy (GRPE). In accordance with the provisions of paras. 6.3.4.2, 6.3.7 and 6.4 of the 1998 Agreement, this document shall be appended to the amended gtr once adopted.

I.		Background

1.	On 23 August 2013, the informal group for the development of the Worldwide harmonized Light vehicles Test Procedures (WLTP) submitted a draft text of the WLTP global technical regulation (gtr) (ECE/TRANS/WP.29/GRPE/2013/13) to the Working Party on Pollution and Energy (GRPE) of the World Forum for Harmonization of Vehicle Regulations (WP.29).

2.	ECE/TRANS/WP.29/GRPE/2013/13, as amended by GRPE-67-04-Rev.1, was adopted by GRPE at is sixty-seventh session, held on 14 November 2013. WP.29 will consider the resulting text in March 2014 (ECE/TRANS/WP.29/2014/27).

3.	The text adopted by GRPE reflects the work concerning "Phase 1a" draft of the WLTP gtr development. This covers the development of a globally harmonised test cycle for light duty vehicles and the associated test procedures, as outlined in the official document ECE/TRANS/WP.29/2009/131 (Phase 1 of the WLTP process). The preparation of this text followed a four months extension of the work and required the additional session of GRPE in November 2013, as recognized by WP.29 in its 156th session (March 2012). The current mandate of the WLTP informal working group ended with the submission of this draft to GRPE.

II.	Proposal, draft roadmap and extension of the mandate of the WLTP informal working group

4.	The current WLTP gtr describes a complete certification test cycle. Nevertheless, the "Phase 1a" draft of the WLTP gtr does not include a number of technical elements that could significantly improve the application of this regulatory text. An extension of the mandate for the WLTP informal working group, sponsored by the European Union and Japan, shall tackle the development of these technical elements. This task should be labelled as "Phase 1b" and is foreseen to last until 2016.

5.	A road map and a possible substructure of the WLTP informal working group are shown in Figure 1. Figure 2 contains an indicative list of issues that will be addressed during "Phase 1b".

6.	In addition to the tasks explicitly mentioned in Figure 2, the WLTP informal working group shall also address, during its mandate period, any other task that is deemed relevant for the development of the globally harmonized test cycle for light duty vehicles and the associated test procedures. The WLTP informal working group may also choose its internal structure and management, such as Chairs and secretaries, according to its needs.

# Figure 1

# WLTP informal working group: organization

# Figure 2

# WLTP "Phase 1b": indicative roadmap

# Footnotes

*	In accordance with the programme of work of the Inland Transport Committee for 2012–2016 (ECE/TRANS/224, para. 94 and ECE/TRANS/2012/12, programme activity 02.4), the World Forum will develop, harmonize and update Regulations in order to enhance the performance of vehicles. The present document is submitted in conformity with that mandate.