Proposal for Supplement 8 to the 04 series of amendments to Regulation No. 44

- Proposal

Paragraph 6.1.5., amend to read

"6.1.5.	The child restraint manufacturer has to declare in written form that the toxicity of materials used in the manufacture of restraint systems and accessible to the restrained child is in conformity with the relevant parts of CEN Safety of Toys, part 3 (June 1982).  EN 71:2009, part 3. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority. This paragraph does not apply to restraint devices of groups II and III.

Paragraph 6.1.6., amend to read

"6.1.6.	The child restraint manufacturer has to declare in written form that the flammability of materials used to manufacture the restraint system is in conformity with the relevant paragraph of the Consolidated Resolution on the Construction of Vehicles (R.E.3) (document ECE/TRANS/WP.29/78/Rev.2, paragraph 8.23.) parts  of EN 71:2009 part 2. Tests confirming the validity of the declaration may be carried out at the discretion of the test authority.

Correspondent Footnote to be removed

The address to obtain the relevant CEN standards is: CEN, 2 rue Bréderode, B.P. 5, B 1000 Bruxelles, Belgium.

II.	Justification

It necessary to align the corresponding prescription of Regulation No. 129 and this regulation.