UN/SCETDG/47/INF.8

| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals 26 May 2015 |
| --- |
| Sub-Committee of Experts on the Transport of Dangerous Goods |  |
| Forty-seventh session |  |
| Geneva, 22 – 26 June 2015 Item 2 (i) of the provisional agenda Explosives and related matters: miscellaneous |  |

Transport of PENTAERYTHRITE TETRANITRATE (PETN) with less than 25 % of water but more than 9% of water

Transmitted by the expert from Spain

Introduction

- The purpose of this paper is to share the Spanish experience on transport of PETN under UN 0150 with less than 25% of water. For UN 0150 Special Provision 266 is assigned, which grants the possibility of carrying this substance with a lower percentage of water under the specific approval by a Competent Authority.

- Transport of PETN has been authorised by the Spanish Competent Authority for several years with a percentage of water in between 9 and 25%.

Background

3.	The UN Model Regulations contain three entries for the transport of PETN: UN 0150, UN 0411 and UN 3344, this last as class 4.1 “mixture, desensitized, solid”. From an industrial point of view and as raw material to produce other civil explosives, like detonators or detonating cord, only UN 0150 can be used, taking into account that UN 3344 is not possible for economic reasons and that UN 0411 includes a minimum contents of wax.

4.	In December of 2010 the Spanish Authority granted an approval to transport PETN with less than 25 % but more than 9% of water in mass by road. This approval was based on the negative results of tests series 3 provided by the applicant, which were carried out by a European Notified Body (Official European Testing Laboratory). The approval was extended for periods of one year on 2011, 2012, 2013, 2014 and 2015. Additionally, the Spanish Maritime Authority also granted an approval in March 2014 to transport PETN with less than 25% but more than 9% of water by sea, based on the same tests series 3 results.

5.	During the aforesaid years more than 4.000 tons of PETN were transported without any problem and/or incident, both, at national and international level, by road and by sea.

Proposal

6.	As a consequence of the abovementioned information the purpose of this paper is to provide a basis for discussion, before sending an official paper, on the possibility of allowing the transport of PETN with less than 25 % water by mass, but with more than 9% of water by mass.

7.	To avoid increasing the number of entries in the UN Model Regulations, and also to be compatible with the current separation in between UN 0150 and UN 0411, it is proposed to modify the entry for UN 0411 and to include there the possibility of a lower percentage of water. This would mean the following modifications for UN 0411:

In column (2) “Name and description” add “…or 9% water…”

In column (8) “Packing instruction” add…. P112(a)

8.	Therefore the Dangerous Good List for UN 0411 would be as follows (new text underlined):

9.	Additionally, Special Provision SP 131 should be modified as follows (new text underlined):

SP131		The phlegmatized or wetted substance shall be significantly less sensitive than dry PETN.

Justification

10.	No safety implications are foreseen. Transport during the last 5 years has been carried out under similar conditions, in accordance with an approval of a National Competent Authority.

11.	In the annex the results of tests series 3 provided by the applicant, which were carried out by a European Notified Body, are included.

Annex: Test series 3 results

PETN with 9% of water

Test 3 a) 	Sensitiviness to impact

3 a ii) 		BAM Fallhammer

| Fall Height (cm) | Weight (kg) | Number of trials | Positive Results |
| --- | --- | --- | --- |
| 60 50 40 40 | 5 5 5 5 | 3 4 6 6 | 1 1 0 0 |

Sensitiviness to impact > 25J

Temperature during the trials: 25,1 +- 2,5 ºC

Room Humidity: 47 %

Test 3 b) Sensitiviness to friction

3 b 		BAM friction apparatus

| Load (N) | Number of trials | Positive Results |
| --- | --- | --- |
| 160 120 80 60 | 2 3 6 6 | 1 1 1 0 |

Sensitiviness to friction: 80 N

Temperature during the trials: 21,5 +- 2,5 ºC

Room Humidity: 48 %

Test 3 c) 	Thermal stability at 75 ºC

No reaction

Test 3 d) 	Response to a fire

3 d 		Small scale burning test

Kraft paper and simple base powder

Initiation: Safety fuse

| Trial | Weighjt (g) | Result |
| --- | --- | --- |
| 1 2 3 4 | 10 10 100 100 | No inflammation No Inflammation No Inflammation No Inflammation |