UN/SCETDG/47/INF.27

| Committee of Experts on the Transport of Dangerous Goods and on the Globally Harmonized System of Classification and Labelling of Chemicals 10 June 2015 |
| --- |
| Sub-Committee of Experts on the Transport of Dangerous Goods |  |
| Forty-seventh session |  |
| Geneva, 22 – 26 June 2015 Item 3 of the provisional agenda Listing, classification and packing |  |

Additional criteria for polymerizing substances

Transmitted by the European Chemical Industry Council (CEFIC)

Introduction

- During the last session of the Sub-Committee of Experts on the Transport of Dangerous Goods (TDG Sub-Committee), it was decided to introduce a new division 4.1 for polymerizing substances.

- In 2.4.2.5.1, the definition describes polymerizing substances as “substances which, without stabilization, are liable to undergo a strongly exothermic reaction resulting in the formation of larger molecules or resulting in the formation of polymers under conditions normally encountered in transport.“

- However, given that the energy criterion of more than 300 J/g is met, in-depth chemical knowledge is required to understand and  assess whether a substance is able to polymerize, rearrange or decompose (and, in the latter case, be a candidate for classification as a self-reactive substance), and to come to the correct conclusion about the classification.

- Therefore, industry believes it would be helpful to introduce some provisions that are scientifically sound and simple to apply in order to correctly identify substances that should be classified as polymerizing.

- Members of the Subcommittee are requested to review this paper and to forward any comments to the CEFIC delegation who intends to submit a formal proposal in this matter for the December session.

Discussion

- In most chemical textbooks, the ability to polymerize is linked to the existence of unsaturated (i.e. double or triple) bonds or strained rings in the molecule. Thus, polymerization is essentially the formation of a large molecule by addition of small reactive units – the so-called monomers – to the activated end of a growing chain.

- However, the presence of strained rings or unsaturated bonds by themselves does not constitute that a substance will necessarily polymerize. In fact, many substances with such functional groups will not form large molecules by polymerization. Some examples are shown below:

- In general, only rather small molecules will polymerize since the formation of chains becomes more unlikely due to steric reasons in larger molecules. As a second effect, the kinetic frequency factor for the chain-building mechanism drops significantly with increasing size of the molecule, and chain interruption reactions becomes more likely.

- Further, polymerization will not take place in the solid state since a molecule in a crystal lattice will not have the freedom to carry a chain-building mechanism.

- A practical difficulty is the fact that measurement of energy (for example, by DSC according to 20.3.3.3 of the UN Manual of Tests and Criteria) does not distinguish between contributions due to decomposition or polymerization. In general, decomposition becomes predominant with increasing molecular size.

- In order to challenge the statements made above, a broad variety of substances in the market which are known to have the potential of polymerization – many of them with individual UN numbers – has been investigated (see table 1).

- It is found that with increasing size of the molecule the heat of polymerization will drop significantly. This can be explained easily since the energy of the reactive functional groups is released in ratio to the molecular mass.

- However, the molecular mass in itself is not the optimal criterion because some “heavy” atoms like chlorine, bromine and silicon will substantially increase the molecular weight whereas the molecule remains rather small (see for example Bromopropyne, Vinylbromide, Vinyltrichlorosilane). Therefore, it is suggested to take only the elements C, H, O and N into account as a criterion for the size of the molecule. Thus M(CHON) is the molecular mass counting only the contributions of these elements.

- A plot of the polymerization energy versus M(CHON) shows nicely the decrease of the maximum energy with increasing size of the molecule. In fact, none of the compounds exhibits a M(CHON) value of 150 g/mol, and the maximum energy approaches the 300 J/g border value (see figure 1)

Proposal

- In the UN  Manual of Tests and Criteria, appendix 6 (Screening Procedures), insert a chapter 5.2 as follows:

5.2 	Substances which may be polymerizing substances (Division 4.1)

The classification procedure for polymerizing substances need not be applied if

(a)	the chemical structure of the substance contains no double or triple bonds or strained rings,

(b)	or, the compounds contains double or triple bonds or strained rings, but the molecular mass M(CHON) counting only the elements C, H, O and N is more than 150,

(c)	The compound is solid with a melting point above (50 °C)

- Renumber the existing chapters 5.2 to 5.3 and 5.3 to 5.4

Justification

This proposal helps to identify substances that fulfill the classification criteria and gives clear cutoff criteria, thus avoiding confusion and unnecessary testing.

Table 1 Molecular mass and heat of polymerization of known substances

# Text boxes

Figure 1: Correlation between energy and molecular mass M(CHON)