Amendment to Regulation No. 106 - Rev.2 - Tyres for agricultural vehicles

The modifications to the existing text of the Regulation are marked in bold for new or strikethrough for deleted characters.

I.	Proposal

In Annex 7- 	Variation of load capacity with speed, amend to read:

" Part A: Drive wheel tyres for agricultural tractors

Applicable to tyres classified with categories of use: "Tractor drive wheel" (see paragraph 2.20. of this Regulation)

# Variation of load carrying capacity (per cent)

| Speed (km/h) | Speed category symbol |  |  |
| --- | --- | --- | --- |
|  | A2 | A6 (+) | A8 (+) | D (+) |  | (1) |
| 10 | [0] | +40 | +50 | +50 |  | + 58 |
| 15 | -6 | +30 | +34 | +34 |  | + 32 |
| 20 | -11 | +20 | +23 | +23 |  | + 26 |
| 25 | -16 | +7 | +11 | +18,5 |  | + 19 |
| 30 | -20 | [0] | +7 | +15 |  | + 12 |
| 35 | -24 | - 510 | +3 | +12 |  | + 10 |
| 40 | -27 | - 1020 | [0] | +9,5 |  | + 6 |
| 45 | - | - | -4 | +7 |  | + 2 |
| 50 | - | - | -9 | +5 |  | [0] |
| 55 | - | - | - | +3 |  | - |
| 60 | - | - | - | +1,5 |  | - |
| 65 | - | - | - | [0] |  |  |
| 70 | - | - | - | -9 |  | - |

"

II.	Justification

The proposal aim to align the UN Regulation 106 with international standards (ETRTO, T&RA and ISO 4351-2 table 2). This proposal will also avoid any possible misunderstanding for the application of the EC Regulation 167/2013 that refers to UN Reg. 106.