Correction to GRE/2018/05 on Transitional Provisions section

I.	Proposal

Add a new paragraph 13.2.4. and renumber the previous paragraph:

“13.2.4.		Notwithstanding paragraph 13.2.2. and 13.2.3, Contracting Parties applying the UN Regulation shall continue to accept ESA UN type-approvals issued according to the preceding series of amendments to the UN Regulation, for component or separate technical unit which doesn’t include a coupling part to charge the REESS which are not affected by the changes introduced by the 06 series of amendments

13.2.45.	Contracting Parties applying this UN Regulation shall not refuse to grant UN type-approvals according to any preceding series of amendments to this UN Regulation or extensions thereof.”

II.	Justification

- The proposed informal document for TPs included the whole new proposal based on the one in ECE-TRANS-WP29-GRE-2018-05e with only 2 modifications: addition of new clause 13.2.4. and renumbering of previous clause 13.2.4. to 13.2.5.

- New proposed Clause 13.2.4. is proposed for consistency with clause 13.1.4. (TPs for R10.05) with the difference that this could only apply for ESA type approval because ESA measurements and requirements are not affected by the changes introduced by the 06 series of amendments (when vehicle measurements and requirements are affected due to the propose change of vehicle radiated emission narrowband limit). Therefore this new paragraph has been adapted from 13.1.4. keeping only ESA and not vehicle

- Clause 13.2.5. is only a renumbering of previous clause 13.2.4. from ECE-TRANS-WP29-GRE-2018-05e.