E/ECE/324                      Rev.1/Add.59/Amend.2

E/ECE/TRANS/505

1 October 2004

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 59:  Regulation No. 60

## Amendment 2

#### Supplement 2 to the original version of the Regulation - Date of entry into force:  12 August 2004

Uniform provisions concerning the approval of two-wheeled motor cycles and mopeds with regard to driver-operated controls including the identification of controls,
tell-tales and indicators

_________

### UNITED NATIONS

Paragraph 6.2.2.2.1., amend to read:

"6.2.2.2.1.	Vehicles equipped with riding pedals must, and vehicles equipped with a platform or with footrests integrated into a platform may, conform to the requirement.

Position of control: on handlebars: left side forward

Type of control: hand lever."

____________

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.