|  | E/ECE/324/Rev.1/Add.52/Rev.3/Corr.1−E/ECE/TRANS/505/Rev.1/Add.52/Rev.3/Corr.1 |
| --- | --- |
|  |  | 27 August 2013 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 52 – Regulation No. 53

Revision 3 - Corrigendum 1

Corrigendum 1 to Supplement 13 to the 01 series of amendments – Date of entry into force: 26 June 2013

Uniform provisions concerning the approval of category L3 vehicles with regard to the installation of lighting and light-signalling devices

_________

UNITED NATIONS

Paragraph 5.13., correct to read (reinsertion of the last line):

"5.13. 		Colours of the lights

The colours of the lights referred to in this Regulation shall be as follow:

Driving-beam headlamp: 			white

Passing-beam headlamp:			white

Direction-indicator lamp: 			amber

Stop lamp: 					red

Rear-registration plate lamp: 		white

Front position lamp: 				white or amber

Rear position lamp: 				red

Rear retro-reflector, non-triangular: 	red

Side retro-reflector, non-triangular: 	amber at the front

amber or red at the rear

Vehicle-hazard warning signal: 		amber

Front fog lamp : 				white or selective yellow

Rear fog lamp : 				red

Daytime running lamp			white."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.