|  |  | 6 December 2012 |
| --- | --- | --- |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 73: Regulation No. 74

Revision 2 – Amendment 1

Supplement 7 to the 01 series of amendments - Date of entry into force: 18 November 2012

Uniform provisions concerning the approval of category L1 vehicles with regard to the installation of lighting and light-signalling devices

UNITED NATIONS

Paragraph 6.2.1.(a), insert a new footnote *, to read:

"6.2.	Passing beam headlamp

6.2.1. 	Number

One or two of approved type according to:

(a)	Regulation No. 113*;

(b)	Class A of Regulation No. 112;

(c)	Regulation No. 1;

(d)	Regulation No. 56;

(e)	Regulation No. 57;

(f)	Regulation No. 72;

(g)	Regulation No. 76

(h)	Regulation No. 82.

________________

*	Headlamps of Class A of Regulation No. 113 with LED modules only on vehicles with a maximum design speed not exceeding 25 km/h."

________________

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.