|  | E/ECE/324/Rev.2/Add.115/Amend.4−E/ECE/TRANS/505/Rev.2/Add.115/Amend.4 |
| --- | --- |
|  |  | 6 August 2013 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 115 – Regulation No. 116

Amendment 4

Supplement 4 to the original version of the Regulation – Date of entry into force: 15 July 2013

Uniform provisions concerning the protection of motor vehicles against unauthorized use

_________

UNITED NATIONS

Annex 9,

Paragraph 1., amend to read:

"1.	Method ISO

…

Immunity against radiated high frequency disturbances

Testing of the immunity of a VAS/AS in a vehicle may be performed according to the technical prescriptions and transitional provisions of Regulation No. 10, 04 series of amendments and test methods described in Annex 6 for the vehicles and Annex 9 for a separate technical unit.

…

Radiated emissions

Tests shall be performed according to the technical prescriptions and transitional provisions of Regulation No. 10, 04 series of amendments and according to the test methods described in Annexes 4 and 5 for vehicles or Annexes 7 and 8 for a separate technical unit."

Paragraph 2., amend to read:

"2.	Method IEC

…

Radiated emissions

The VAS/AS shall be subjected to testing for the suppression of radio frequency interference according to the technical prescriptions and transitional provisions of Regulation No. 10, 04 series of amendments and according to test methods described in Annexes 4 and 5 for vehicles and Annexes 7 and 8 for a separate technical unit."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.