|  |  | 6 December 2012 |
| --- | --- | --- |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 118: Regulation No. 119

Revision 1 – Amendment 1

Supplement 1 to the 01 series of amendments - Date of entry into force: 18 November 2012

Uniform provisions concerning the approval of cornering lamps for power-driven vehicles

UNITED NATIONS

Paragraphs 8. to 8.2., shall be deleted and replaced by a new paragraph 8., to read:

"8.	Colour of light emitted

The colour of the light emitted inside the field of the light distribution grid defined in paragraph 2. of Annex 3 shall be white. For testing see Annex 4 to this Regulation.  Outside this field, no sharp variations of colour shall be observed."

Annex 4,

Paragraph 1., amend to read:

"1. 	For checking the colorimetric characteristics, a source of light at a colour temperature of 2,856 K, corresponding to illuminant A of the international commission (CIE), shall be used.  For lamps equipped with non-replaceable light sources (filament lamps and other), or light sources (replaceable or non-replaceable) operated together with an electronic light source control gear, the colorimetric characteristics should be verified with the light sources present in the lamp, in accordance with paragraph 7. of this Regulation."

________________

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.