|  | E/ECE/324/Rev.2/Add.120/Rev.1/Amend.4−E/ECE/TRANS/505/Rev.2/Add.120/Rev.1/Amend.4 |
| --- | --- |
|  |  | 6 August 2013 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 120 – Regulation No. 121

Revision 1 - Amendment 4

Supplement 8 to the original version of the Regulation – Date of entry into force: 15 July 2013

Uniform provisions concerning the approval of vehicles with regard to the location and identification of hand controls, tell-tales and indicators

_________

UNITED NATIONS

Insert a new paragraph 5.2.10., to read:

"5.2.10.	Automatic functions may be indicated with the symbol relevant for the corresponding item as referred to in column 1 of Table 1, with the supplementary letter(s) "A" or "AUTO" positioned on or adjacent to its outline."

Table 1, amend to read (including the deletion of footnote 20):

"

| No. | Column 1 | Column2 | Column3 | Column4 | Column5 |
| --- | --- | --- | --- | --- | --- |
|  | Item | Symbol 2 | Function | Illumination | Colour |
| … | … | … | … | … | … |
| 3b | Automatic main beam functions | or 1, 6, 13 | Control | No | - |
|  |  |  | Tell-tale | Yes | - |
| … | … | … | … | … | … |
| 25. | Brake system malfunction | 8 | Tell-tale | Yes | See Regulation Nos. 13-H and 13 as appropriate |
| … | … | … | … | … | … |
| 28. | Parking brake | 9 | Tell-tale | Yes | See Regulation Nos. 13-H and 13 as appropriate |
| … | … | … | … | … | … |

…"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.