|  |  | 27 November 2013 |
| --- | --- | --- |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 44: Regulation No. 45

Revision 2 – Amendment 2

Supplement 8 to the 01 series of amendments - Date of entry into force: 3 November 2013

Uniform provisions concerning the approval of headlamp cleaners, and of power-driven vehicles with regard to headlamp cleaners

UNITED NATIONS

Paragraph 3.3.5., amend to read:

"3.3.5. 	For each type of headlamp, one sample intended for the installation on the left side of the vehicle and one sample intended for the installation of the right side of the vehicle, complete with relevant headlamp(s) installed as described in paragraph 3.3.1. above, either on (a) suitable test fixture(s) or on (a) vehicle(s) representative of the type(s) to be approved, in such a manner as to allow normal operation of the cleaner and the headlamp(s). In the case of headlamps for right hand traffic and left hand traffic, it is sufficient to test only one set of headlamps for either right hand traffic or for left hand traffic;"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.