|  |  | 27 November 2013 |
| --- | --- | --- |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 66: Regulation No. 67

Revision 3 – Amendment 2

Supplement 12 to the 01 series of amendments - Date of entry into force: 3 November 2013

Uniform provisions concerning the approval of:

I.	Specific equipment of vehicles of category M and N using liquefied petroleum gases in their propulsion system

II.	Vehicles of category M and N fitted with specific equipment for the use of liquefied petroleum gases in their propulsion system with regard to the installation of such equipment

UNITED NATIONS

Paragraph 2.1.3., amend to read:

"2.1.3.	"Working pressure (WP)" means the maximum … is determined."

Annex 3,

Paragraphs 5.2. to 5.4., amend to read:

"5.2.	Component classification (according to Figure 1, para. 2):

Class 0 for the part which is in contact with liquid LPG at a pressure > 3,000 kPa;

Class 1 for the part which is in contact with liquid LPG at a pressure ≤ 3,000 kPa.

5.3.	Classification pressure:

Parts of Class 0	WP declared

Parts of Class 1	3,000 kPa

5.4.	Design temperatures:	-20 °C to 65 °C

For temperatures exceeding the above-mentioned values, special tests conditions are applicable."

Annex 8,

Paragraph 4.5.5.3., amend to read:

"4.5.5.3.	The burst pressure shall not be less than 10,000 kPa and at least 2.25 WP."

Annex 15,

Paragraph 5.3., Table 3, amend to read:

# "Table 3

# The classification and leakage test pressures according to the classification:

| Classification of component | Classification pressure [kPa] | Test pressure for leakage test [kPa] |
| --- | --- | --- |
| Class 0 | WP | 1.5 WP |
| Class 1 | 3,000 | 4,500 |
| Class 2A | 120 | 180 |
| Class 2 | 450 | 675 |
| Class 3 | 3,000 | 6,750 |

"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.