|  | E/ECE/324/Rev.1/Add.73/Rev.2/Amend.2−E/ECE/TRANS/505/Rev.1/Add.73/Rev.2/Amend.2 |
| --- | --- |
|  |  | 17 October 2014 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 73 – Regulation No. 74

Revision 2 - Amendment 2

Supplement 8 to the 01 series of amendments – Date of entry into force: 9 October 2014

Uniform provisions concerning the approval of category L1 vehicles with regard to the installation of lighting and light-signalling devices

_________

UNITED NATIONS

Insert a new paragraph 2.5.14., to read:

"2.5.14. 	"Hazard warning signal" means the simultaneous operation of all of a vehicle's direction-indicator lamps to show that the vehicle temporarily constitutes a special danger to other road users;"

Paragraph 5.13., amend to read (footnote 3 remains unchanged):

"5.13. 	Colours of the lights3

The colours of the lights referred to in this Regulation shall be as follows:

Driving-beam headlamp: 			white

Passing-beam headlamp: 			white

Front retro-reflector non triangular: 	white

Side retro-reflector, non-triangular:		amber at the front

amber or red at the rear

Pedal retro-reflector: 			amber

Rear retro-reflector, non-triangular:	red

Direction-indicator lamp: 			amber

Stop lamp: 					red

Rear position lamp:				red

Rear-registration plate lamp: 		white

Vehicle-hazard warning signal:		amber"

Insert a new paragraph 5.15.5., to read:

"5.15.5. 	Vehicle-hazard warning signal (paragraph 6.12.)"

Insert new paragraphs 6.12. to 6.12.4., to read:

"6.12.	Vehicle-hazard warning signal

6.12.1.	The signal shall be given by simultaneous operation of the direction-indicator lamps in accordance with the requirements of paragraph 6.8. above.

6.12.2.	Electrical connections

The signal shall be given by means of a separate control enabling all the direction-indicators to be supplied with current simultaneously.

6.12.3.	"Circuit-closed" tell-tale

Mandatory flashing red signal lamp or, in the case of separate tell-tales, the simultaneous operation of the tell-tale prescribed in paragraph 6.8.11.

6.12.4.	Other requirements

Light flashing 90 ± 30 times per minute.

Operation of the lamp-signal control shall be followed within not more than one second by the appearance of the light and within not more than one-and-a-half seconds by the first extinction of the light."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.