|  | E/ECE/324/Rev.1/Add.90/Rev.3/Corr.1−E/ECE/TRANS/505/Rev.1/Add.90/Rev.3/Corr.1 |
| --- | --- |
|  |  | 13 March 2015 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 90:  Regulation No. 91

Revision 3 – Corrigendum 1

Corrigendum 1 to Revision 3 of the Regulation (Erratum by the secretariat)

Uniform provisions concerning the approval of side-marker lamps for motor vehicles and their trailers

_________

UNITED NATIONS

Paragraph 7.1., the table, footnote 1, correct to read:

"1  In addition, for red side-marker lamp, in the angular field from 60° to 90° in horizontal direction and  ±20° in vertical direction towards the front of the vehicle, the maximum intensity is limited to 0.25 cd."

# Footnotes

*	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.