|  | E/ECE/324/Rev.2/Add.116/Rev.2/Amend.3−E/ECE/TRANS/505/Rev.2/Add.116/Rev.2/Amend.3 |
| --- | --- |
|  |  | 27 November 2013 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 116 – Regulation No. 117

Revision 2 - Amendment 3

Supplement 3 to the 02 series of amendments – Date of entry into force: 3 November 2013

Uniform provisions concerning the approval of tyres with regard to rolling sound emissions and/or to adhesion on wet surfaces and/or to rolling resistance

_________

UNITED NATIONS

Annex 6,

Paragraph 6.2., amend to read:

"6.2.	Temperature correction

If measurements at temperatures other than 25 (C are unavoidable (only temperatures not less than 20 (C or more than 30 (C are acceptable), then a correction for temperature shall be made using the following equation, with:

Fr25	is the rolling resistance at 25 (C, in Newton:

| Where: |  |
| --- | --- |
|  | is the rolling resistance, in Newton, |
|  | is the ambient temperature, in degree Celsius, |
|  | is equal to: 0.008 for Class C1 tyres 0.010 for Class C2 and C3 tyres with a load index equal or lower than 121 0.006 for Class C3 tyres with a load index greater than 121" |

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.