|  | E/ECE/324/Rev.2/Add.117/Rev.1/Amend.1−E/ECE/TRANS/505/Rev.2/Add.117/Rev.1/Amend.1 |
| --- | --- |
|  |  | 27 November 2013 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 117 – Regulation No. 118

Revision 1 - Amendment 1

Supplement 1 to the 02 series of amendments – Date of entry into force: 3 November 2013

Uniform technical prescriptions concerning the burning behaviour and/or the capability to repel fuel or lubricant of materials used in the construction of certain categories of motor vehicles

_________

UNITED NATIONS

Paragraph 2.2., amend to read:

"2.2.		"Interior compartment" means any compartment intended for passengers, drivers and/or crew bounded by the interior facing surface(s) of:

(a)	The ceiling;

(b)	The floor;

(c)	The front, rear and side walls,

(d)	The doors;

(e)	The outside glazing."

Paragraph 5.2.1., amend to read:

"5.2.1.	The materials inside and no more than 13 mm beyond the interior compartment, materials of the engine compartment and materials of any separate heating compartment used in the vehicle to be type approved shall meet the requirements of Part II of this Regulation."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.