|  | E/ECE/324/Rev.2/Add.122/Rev.2/Amend.2−E/ECE/TRANS/505/Rev.2/Add.122/Rev.2/Amend.2 |
| --- | --- |
|  |  | 20 October 2014 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 122 – Regulation No. 123

Revision 2 - Amendment 2

Supplement 6 to the 01 series of amendments – Date of entry into force: 9 October 2014

Uniform provisions concerning the approval of adaptive front-lighting systems (AFS) for motor vehicles

_________

UNITED NATIONS

Paragraph 6.2.5.2., shall be deleted.

Paragraphs 6.2.5.3. to 6.2.5.5.1. (former), renumber as paragraphs 6.2.5.2. to 6.2.5.4.1.

Paragraph 6.3.4.1., amend to read:

"6.3.4.1. 	The lighting unit(s) of the right side and of the left side each provide at least 16,200 cd at the point HV."

Annex 3,

Table 1, delete the footnote 6 and its reference and renumber the subsequent footnotes accordingly.

Annex 9,

Paragraph 1.8.1., amend to read:

"1.8.1.	However in those cases where a provision is specified for one side only, the division by the factor of 2 does not apply. These cases are: paragraphs 6.2.5.2., 6.2.8.1., 6.3.2.1.1., 6.3.2.1.2., 6.3.4.1., 6.4.6. and footnote 4 of Table 1 of Annex 3"

Paragraph 3.1.1.1., amend to read:

"3.1.1.1. 	Compliance with the requirements of paragraphs 6.2.5.2. and 6.2.5.4.1. of this Regulation shall be checked for both Category 1 and Category 2 bending modes without additional horizontal re-aim."

Annex 11,

Paragraph 5., amend to read:

"5.	The measurement of the objective luminous flux of LED module(s) producing the class C (basic) passing-beam shall be carried out as follows:"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.