| E/ECE/324 E/ECE/TRANS/505 |  | Rev.1/Add.42/Rev.2/Amend.3/Corr.1 |
| --- | --- | --- |
| 20 March 2008 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments which entered into force on 16 October 1995)

_________

Addendum 42:  Regulation No. 43

## Revision 2 - Amendment 3 - Corrigendum 1

#### Corrigendum 1 to Supplement 10 to the original version of the Regulation, subject of Depositary Notification C.N.1156.2007.TREATIES-1 dated 18 January 2008

Uniform provisions concerning the approval OF safety glazing materials and their installation on vehicles

_________

### UNITED NATIONS

Annex 3,

Paragraph 9.1.2.2., amend to read (footnote 8/ not amended):

"9.1.2.2.	For the windscreens of M1 vehicles 8/

the test shall be carried out in test area B defined in Annex 18, paragraph 2.3., excluding any opaque obscuration impinging on it.

For the windscreens of N1 vehicles, the manufacturer may request that the same test may be carried out either in test area B defined in Annex 18, paragraph 2.3., excluding any opaque obscuration impinging on it, or in the zone I defined in paragraph 9.2.5.2.3. of this annex.

For windscreens of other categories .… "

Paragraph 9.2.2.1., amend to read:

"9.2.2.1.	For vehicle category M1 in test area A, extended to the median plane of the vehicle, and in the corresponding part of the windscreen symmetrical to it about the longitudinal median plane of the vehicle, and also in the reduced test area B according to paragraph 2.4. of Annex 18."

Paragraph 9.2.2.2., amend to read:

"9.2.2.2.	For vehicles of categories M and N other than M1:

(a)	in zone I as defined in paragraph 9.2.5.2. of this annex for M2, M3, N2 and N3 vehicles;

(b)	either in zone I as defined in paragraph 9.2.5.2. of this annex or in test area A, extended to the median plane of the vehicle, and in the corresponding part of the windscreen symmetrical to it about the longitudinal median plane of the vehicle, and also in the reduced test area B according to paragraph 2.4. of Annex 18 for N1 vehicles."

Paragraph 9.2.5.1., amend to read:

"9.2.5.1.	Zones A and B of windscreens for vehicle category M1 and N1 are defined in Annex 18 to this Regulation."

Paragraph 9.2.5.2., amend to read:

"9.2.5.2.	Zones of windscreens for vehicles of categories M and N other than M1 are defined on the basis of:"

Paragraph 9.2.6., the table, the text in the second row of the first column, amend to read:

"M1 and N1."

Paragraph 9.2.6., the table, the text in the third row of the first column, amend to read:

"M and N categories other than M1"

Paragraph 9.3.5., the table, the text in the second row of the first column, amend to read:

"M1 and N1."

Paragraph 9.3.5., the table, the third row of the first column, amend to read:

"M and N categories other than M1"

Annex 18, the title, amend to read:

"PROCEDURE FOR DETERMINING TEST AREAS ON WINDSCREENS OF VEHICLES IN RELATION TO THE "V" POINTS"

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

GE.08-21952