| E/ECE/324 E/ECE/TRANS/505 |  | Rev.1/Add.42/Rev.2/Amend.3 |
| --- | --- | --- |
| 15 January 2008 |  |  |

# AGREEMENT

CONCERNING THE ADOPTION OF UNIFORM TECHNICAL PRESCRIPTIONS
FOR WHEELED VEHICLES, EQUIPMENT AND PARTS WHICH CAN BE FITTED
AND/OR BE USED ON WHEELED VEHICLES AND THE CONDITIONS FOR RECIPROCAL RECOGNITION OF APPROVALS GRANTED ON THE BASIS OF THESE PRESCRIPTIONS (/

(Revision 2, including the amendments that entered into force on 16 October 1995)

_________

Addendum 42:  Regulation No. 43

## Revision 2 - Amendment 3

#### Supplement 10 to the original version of the Regulation - Date of entry into force:  10 November 2007

Uniform provisions concerning the approval OF safety glazing materials and their installation on vehicles

_________

### UNITED NATIONS

Annex 3,

Paragraph 9.1.2.2., amend to read (including footnote 8/):

"9.1.2.2.	For windscreens of M1 vehicles and N1 8/ vehicles derived from a M1 vehicle, having the same:

(a)	driver's seat reference point

(b)	windscreen dimensional characteristics

(c)	windscreen inclination angle

the test shall be carried out in test area B defined in Annex 18, paragraph 2.3., excluding any opaque obscuration impinging on it.

For windscreens of other categories .…

__________________

8/	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

Paragraph 9.2.2.1., amend to read:

"9.2.2.1.	For windscreens of M1 vehicles and N1 vehicles restricted as described under paragraph 9.1.2.2., in test area A, extended to the median plane of the vehicle, and in the corresponding part of the windscreen symmetrical to it about the longitudinal median plane of the vehicle, and also in the reduced test area B according to paragraph 2.4. of Annex 18."

Paragraph 9.2.2.2., amend to read:

"9.2.2.2.	For windscreens of other categories of vehicles, in zone I as defined in paragraph 9.2.5.2. of this annex."

Paragraph 9.2.5.1., amend to read:

"9.2.5.1.	Zones A and B of windscreens for vehicle category M1 and N1 restricted as described under paragraph 9.1.2.2. are defined in Annex 18 to this Regulation."

Paragraph 9.2.5.2., amend to read:

"9.2.5.2.	Zones of windscreens for other categories of vehicles are defined on the basis of:"

Paragraph 9.2.6., the table, the text in the second row of the first column, amend to read:

"M1 and N1 restricted as described under paragraph 9.1.2.2."

Paragraph 9.2.6., the table, the text in the third row of the first column, amend to read:

"Other categories of vehicles"

Paragraph 9.3.5., the table, the text in the second row of the first column, amend to read:

"M1 and N1 restricted as described under paragraph 9.1.2.2."

Paragraph 9.3.5., the table, the third row of the first column, amend to read:

"Other categories of vehicles"

-----

# Footnotes

(/	Former title of the Agreement:

Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

GE.08-20535