| E/ECE/324/Rev.1/Add.42/Rev.2/Amend.6 −E/ECE/TRANS/505/Rev.1/Add.42/Rev.2/Amend.6 |
| --- |
|  |  | 12 January 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 42: Regulation No. 43

Revision 2 – Amendment 6

Supplement 13 to the original version of the Regulation - Date of entry into force: 
9 December 2010

Uniform provisions concerning the approval of safety glazing materials and their installation on vehicles

UNITED NATIONS

Paragraph 1, amend to read:

"1. 	Scope

This Regulation applies to:

(a)	Safety glazing materials intended for installation as windscreens or other panes, or as partitioning, on vehicles of category L with bodywork, M, N, O, and T1;

(b)	Vehicles of category M, N and O with regard to the installation of these materials;

in both cases, to the exclusion of glazing for lighting and light-signalling devices and instrument panels, of special bullet-proof glazing and of double-windows.

__________________

1	As defined in Annex 7 to the Consolidated Resolution on the Construction of Vehicles (R.E.3), (document TRANS/WP.29/78/Rev.1/Amend.2 as last amended by Amend.4)."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.