| E/ECE/324/Rev.1/Add.42/Rev.2/Amend.7−E/ECE/TRANS/505/Rev.1/Add.42/Rev.2/Amend.7 |
| --- |
|  |  | 12 December 2011 |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 42: Regulation No. 43

Revision 2 – Amendment 7

Supplement 14 to the original version of the Regulation - Date of entry into force: 28 October 2011

Uniform provisions concerning the approval of safety glazing materials and their installation on vehicles

UNITED NATIONS

Insert a new paragraph 2.26., to read:

"2.26.	"Central driving position" is defined when Y co-ordinate of the R point is in Y0 position within + or – 60 mm."

Annex 18,

Paragraph 2.2., amend to read:

"2.2.	"Test area A" is the area of the outer surface of the windscreen bounded by the intersection of the following four planes (see Figures 1a and 1b):

(a)	A plane inclined upwards from the X axis at 3°, passing through V1, and parallel to the Y axis (plane 1);

(b)	A plane inclined downwards from the X axis at 1°, passing through V2, and parallel to the Y axis (plane 2);

(c)	A vertical plane passing through V1 and V2 and inclined at 13° to the left of the X axis in the case of left-hand drive vehicles and to the right of the X axis in the case of right-hand drive vehicles (plane 3);

(d)	A vertical plane passing through V1 and V2 and inclined at 20° to the right of the X axis in the case of left-hand drive vehicles, to the left of the X axis in the case of right-hand drive vehicles (plane 4);

(e)	In case of a single central driving position, two planes upwards and downwards as defined in paragraphs 2.2 (a) and (b) above and two vertical plane passing through V1 and V2 and inclined at 15° to the left of the X axis (plane 3) and 15° to the right of the X axis (plane 4) (see Figure 1b)."

Figure 1, renumber as Figure 1a

Insert a new Figure 1b, to read:

# "Figure 1b

Test area "A" (example of Central Driving Position)

CL:	 trace of the longitudinal median plane of the vehicle

Pi :	 trace of the relevant plane (see text)"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.

# Text boxes

CL

CL

P4

P3

V2

V1

P2

P1