| E/ECE/324/Rev.1/Add.47/Rev.6/Amend.1/Corr.1−E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Amend.1/Corr.1 |
| --- |
|  |  | 14 February 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 47: Regulation No. 48

Revision 6 – Amendment 1 – Corrigendum 1

Corrigendum 1 to Supplement 4 to 04 series of amendments to the Regulation, subject of Depositary Notification C.N.800.2010.TREATIES-15 dated 23 December 2010

Uniform provisions concerning the approval of vehicles with regard to the installation of lighting and light-signalling devices

UNITED NATIONS

Paragraph 2.10., correct to read.

"2.10. 	The "apparent surface" for a defined direction of observation means, at the request of the manufacturer or his duly accredited representative, the orthogonal projection of:

either the boundary of the illuminating surface projected on the exterior surface of the lens;

or the light-emitting surface;

in a plane perpendicular to the direction of observation and tangential to the most exterior point of the lens.  Different examples of the application of apparent surface can be found in Annex 3 to this Regulation.

Only in the case of a light-signalling device producing variable luminous intensities, its apparent surface that may be variable as specified in paragraph 2.7.1.3. shall be considered under all conditions permitted by the variable intensity control, if applicable."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.