| E/ECE/324/Rev.1/Add.47/Rev.6/Amend.3/Corr.1−E/ECE/TRANS/505/Rev.1/Add.47/Rev.6/Amend.3/Corr.1 |
| --- |
|  |  | 7 June 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 47: Regulation No. 48

Revision 6 – Amendment 3 – Corrigendum 1

Corrigendum 1 to Supplement 5 to the 04 series of amendments to the Regulation, subject of Depositary Notification C.N.155.2011.TREATIES-3 dated 28 April 2011

Uniform provisions concerning the approval of vehicles with regard to the installation of lighting and light-signalling devices

UNITED NATIONS

Paragraph 1, modifier comme suit:

Paragraph 5.18.1., amend to read:

"5.18.1.	If at all fixed positions of the movable components the lamps on the movable components meet all the position, geometric visibility, colorimetric and photometric requirements for those lamps."

Paragraph 5.18.4., amend to read:

"5.18.4.	…

(a) 	…  However, additional lamps for the above functions may be activated, when the movable component is in any fixed open position, provided that these additional lamps satisfy all the position, geometric visibility, colorimetric and photometric requirements applicable to the lamps installed on the movable component.

…

(b) 	Should … the interdependent lamp(s) specified by the Applicant during the device approval procedure shall meet all the position, outwards geometric visibility, colorimetric and photometric requirements for those lamps, at all fixed positions of the movable component(s) ..."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.