| E/ECE/324/Rev.1/Add.49/Rev.2/Amend.3−E/ECE/TRANS/505/Rev.1/Add.49/Rev.2/Amend.3 |
| --- |
|  |  | 12 December 2011 |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 49: Regulation No. 50

Revision 2 – Amendment 3

Supplement 15 to the original version of the Regulation - Date of entry into force: 28 October 2011

Uniform provisions concerning the approval of front position lamps, rear position lamps, stop lamps, direction indicators and rear-registration-plate illuminating devices for vehicles of category L

UNITED NATIONS

Paragraph 3.1.2., amend to read:

"3.1.2. 		In the case of a front position lamp an indication whether it is intended to emit white or amber light."

Paragraph 9., amend to read:

"9. 		Colour of light emitted

Stop lamps and rear position lamps shall emit red light, front position lamps may emit white or amber light, direction indicators shall emit amber light. …"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.