| E/ECE/324/Rev.1/Add.57/Rev.2/Amend.1/Corr.1−E/ECE/TRANS/505/Rev.1/Add.57/Rev.2/Amend.1/Corr.1 |
| --- |
|  |  | 3 October 2012 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be fitted and/or be used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 57: Regulation No. 58

Revision 2 – Amendment 1 – Corrigendum 1

Corrigendum 1 to Amendment 1 to Revision 2 of the Regulation - Date of entry into force: 26 July 2012

Uniform provisions concerning the approval of:

I.	Rear underrun protective devices (RUPDs)

II.	Vehicles with regard to the installation of an RUPD of an approved type

III.	Vehicles with regard to their rear underrun protection (RUP)

UNITED NATIONS

Paragraph 2.3., correct to read

"2.3.	Any vehicle in one of the categories M1, M2, M3, N1, O1 or O2 shall be deemed …

Where there is more than one rear axle, the width to be considered is that of the widest.

The requirements of paragraphs 2.3.(b) and 2.3.(c) above shall be satisfied at least on a line:

(a)	At a distance of not more than 450 mm from the rear extremity of the vehicle;

(b)	That may have interruptions totalling not more than 200 mm."

Paragraph 24.1., correct to read:

"24.1.	If the vehicle submitted for approval pursuant to this Regulation meets the requirements of paragraph 2.3.(b) or paragraph 2.3.(c) or paragraph 25 and has been tested following the conditions set out in paragraph 2.2., approval of that vehicle type shall be granted."

Paragraph 31.5., correct to read:

"31.5.	As from 48 months …

(a)	… meets the requirements of paragraph 2.3.(b) or paragraph 2.3.(c) or Part III of this Regulation as amended by the 02 series of amendments;

(b)	… the requirements of paragraph 2.3.(b) or paragraph 2.3.(c) or Part III of this Regulation as amended by the 02 series of amendments.

…."

Annex 3, correct to read:

"Annex 3

….

of a type of a vehicle with regard to its rear underrun protection (RUP) pursuant to paragraph 2.3.(b) / paragraph 2.3.(c) / Part III2 of Regulation No. 58.

_____________

2  Strike out what does not apply."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.