| E/ECE/324/Rev.1/Add.88/Amend.2−E/ECE/TRANS/505/Rev.1/Add.88/Amend.2 |
| --- |
|  |  | 24 February 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 88: Regulation No. 89

Amendment 2

Supplement 2 to the original version of the Regulation - Date of entry into force: 30 January 2011

Uniform provisions concerning the approval of:

I.	Vehicles with regard to limitation of their maximum speed or their adjustable speed limitation function

II.	Vehicles with regard to the installation of a speed limiting device (SLD) or adjustable speed limitation device (ASLD) of an 	approved type

III.	Speed limitation devices (SLD) ) and adjustable speed limitation device (ASLD)

UNITED NATIONS

Paragraph 1.1.1., amend to read:

"1.1.1.		Part I: Vehicles of categories1 M2, M3, N2 and N32 equipped with an SLD and to vehicles of categories M and N equipped with an adjustable speed limitation device ASLD which have not been separately approved according to Part III of this Regulation, or to vehicles so designed and/or equipped that their component parts can be regarded as totally or partially fulfilling the function of an SLD or ASLD, as appropriate."

Paragraph 1.1.2., amend to read:

"1.1.2.	Part II: The installation on vehicles of categories M2, M3, N2 and N3 of SLDs and installation on vehicles of categories M and N of ASLD which have been type approved to Part III of this Regulation."

Paragraph 1.1.3., amend to read:

"1.1.3.	Part III: SLDs which are intended to be fitted to vehicles of categories M2, M3, N2 and N3 and ASLD which are intended to be fitted to vehicles of categories M and N."

Paragraph 1.2.1., amend to read:

"1.2.1.	A speed limitation device (SLD) or function (SLF) shall limit the maximum speed of vehicles of categories M2, M3, N2 and N3."

Paragraph 1.2.2., amend to read:

"1.2.2.	When fitted, the adjustable speed limitation device (ASLD) or function (ASLF) shall limit the speed of vehicles of categories M and N to a speed voluntarily set by the driver when it is activated."

Delete paragraph 1.2.3.

Paragraph 5.1., amend to read:

"5.1.	Requirements for vehicles of categories M2, M3, N2 and N3 equipped with SLF"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.