| E/ECE/324/Rev.1/Add.90/Rev.2/Amend.2−E/ECE/TRANS/505/Rev.1/Add.90/Rev.2/Amend.2 |
| --- |
|  |  | 25 January 2011 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be Fitted and/or be Used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 90: Regulation No. 91

Revision 2 – Amendment 2

Supplement 12 to the original version of the Regulation - Date of entry into force: 
9 December 2010

Uniform provisions concerning the approval of side-marker lamps for motor vehicles and their trailers

UNITED NATIONS

Insert a new paragraph 6.3.3., to read:

"6.3.3.	A light source module shall be so designed that regardless of the use of tool(s), it shall not be mechanically interchangeable with any replaceable approved light source."

Annex 2, item 9., amend to read:

"9.	Concise description3:

…

Light source module specific identification code:

Only for limited mounting height equal to or less than 750 mm above the ground:  yes/no2

Geometrical conditions of installation and relating variations, if any: 	"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.