| E/ECE/324/Rev.2/Add.103/Rev.1/Amend.1−E/ECE/TRANS/505/Rev.2/Add.103/Rev.1/Amend.1 |
| --- |
|  |  | 15 August 2012 |

Agreement

Concerning the Adoption of Uniform Technical Prescriptions for Wheeled Vehicles, Equipment and Parts which can be fitted and/or be used on Wheeled Vehicles and the Conditions for Reciprocal Recognition of Approvals Granted on the Basis of these Prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 103: Regulation No. 104

Revision 1 – Amendment 1

Supplement 7 to the original version of the Regulation - Date of entry into force: 26 July 2012

Uniform provisions concerning the approval of retro-reflective markings for vehicles of category M, N and O

UNITED NATIONS

Annex 7,

Paragraph 1, correct to read:

"When illuminated with a CIE Standard illuminant A and measured as recommended by CIE publication No. 54, 1982, the coefficient of retro-reflection R' in candelas per m2 per lux (cd/m2/lux) of the retro-reflective areas in new condition shall be at least as indicated in table 1 for yellow, white and red materials."

Table 1, correct to read:

# "Table 1

Minimum values for the Coefficient of Retro-reflection R’ [cd.m-2.lx-1]

| Observation angle α [º] | Entrance Angle β [º] |
| --- | --- |
| α=0.33(20’) | β1 | 0 | 0 | 0 | 0 | 0 |
|  | β2 | 5 | 20 | 30 | 40 | 60 |
| Colour |  |  |  |  |  |  |
| Yellow |  | 300 | -- | 130 | 75 | 10 |
| White |  | 450 | -- | 200 | 95 | 16 |
| Red |  | 120 | 60 | 30 | 10 | -- |

"

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.