| E/ECE/324/Rev.2/Add.120/Rev.1/Amend.1−E/ECE/TRANS/505/Rev.2/Add.120/Rev.1/Amend.1 |
| --- |
|  |  | 12 December 2011 |

Agreement

Concerning the adoption of uniform technical prescriptions for wheeled vehicles, equipment and parts which can be fitted and/or be used on wheeled vehicles and the conditions for reciprocal recognition of approvals granted on the basis of these prescriptions*

(Revision 2, including the amendments which entered into force on 16 October 1995)

Addendum 120: Regulation No. 121

Revision 1 – Amendment 1

Supplement 5 to the original version of the Regulation - Date of entry into force: 28 October 2011

Uniform provisions concerning the approval of vehicles with regard to the location and identification of hand controls, tell-tales and indicators

UNITED NATIONS

Table 1, amend to read:

"

| No. | Column 1 | Column 2 | Column 3 | Column 4 | Column 5 |
| --- | --- | --- | --- | --- | --- |
|  | Item | Symbol2 | Function | Illumination | Colour |
| …. | … | … | … | … | … |
| 25. | Brake system malfunction | 8 | Tell-tale | Yes | see Regulations Nos. 13-H and 13 as appropriate |
| …. | … | … | … | … | … |
| 43. | Electronic stability control (including malfunction) | or ESC 17 | Tell-tale | Yes | see Regulations Nos. 13-H and 13 as appropriate |
| …. | … | … | … | … | … |

1	…

17	The vehicle outline shown is not intended to be restrictive, but is the recommended outline.  Alternative vehicle outlines may be used in order to better represent the actual outline of a given vehicle.

18	Symbol may be shown in other colours than specified in column 5 in order to convey different meanings according to the general colour coding as proposed in paragraph 5 of ISO 2575-2004.

19	… lowercase letters."

# Footnotes

*	Former title of the Agreement: Agreement Concerning the Adoption of Uniform Conditions of Approval and Reciprocal Recognition of Approval for Motor Vehicle Equipment and Parts, done at Geneva on 20 March 1958.